## Slide 1: Low Cost SCADA for CyberSecurity Education
Tommy Morris
Professor, Electrical and Computer Engineering
Director, Center for Cybersecurity Research and Education
University of Alabama in Huntsville

## Slide 2: TopICS
What is SCADA?
OpenPLC
Virtual SCADA w/ OpenPLC
Demo

## Slide 3
Flood Control
Water Distribution
Oil/Gas Distribution
Petrochemical
Factory
Automation
Electrification
Critical Infrastructure
Notes: Are there computers here?
Hydraulic drives, gate controls, water level monitoring, etc

## Slide 4: A Common Understanding
Cyber security staff must understand the system/product they are defending.
Product/design engineers must understand implications of poor cyber security.
Cyber security
staff
Product engineers

## Slide 5: The set of computers, networked data communications and graphical user interfaces that monitors and control industrial processes is called SCADA

## Slide 6: What Is SCADA?
Supervisory Control And Data Acquisition
Notes: When controllers are applied to processes like shown before, the system is usually called SCADA

## Slide 7: What Is SCADA?
Supervisory Control And Data Acquisition
Huh?!

## Slide 8: What Is SCADA?
Supervisory Control And Data Acquisition
Supervisory | Control | Data Acquisition
Supervisor synonyms Manager Overseer Administrator | Change current state of process Open close breakers, switches, valves, etc. | Situational Awareness Monitoring

## Slide 9: Substation
Situational Awareness
Control
  Open/close breakers
  Islanding

## Slide 10: Water Distribution
Need to control water level in tower to keep steady water pressure.
Water is pumped in when level is low.

## Slide 11: Oil/Gas Distribution
Monitor Pressure
Route Product
Billing

## Slide 12: Electric Grid
Situational Awareness
Route Power
Billing

## Slide 13: Petrochemical
Follow complex recipe to produce product
Safety
Storage

## Slide 14
Factory: Donor Needle Machine
This machine captured donor needles off the grinder and feed them onto a turntable. Once on the turntable the needles were presented to a machine vision system four at a time for inspection. The system verified the angle of the needle to ensure it was within specification.
Slide from Drew Richey.

## Slide 15
Factory: Airbag Assembly Machine
This machine takes an unfolded airbag cushion and folds it to the highly critical fold specs required for correct deployment. Once it is properly folded a slide advances a sock over the bag to help keep its form.
  A-Pillar
Slide from Drew Richey.

## Slide 16
Factory: Traceability System
Auto manufacturing
JIT manufacturing
DOT Federal mandate (seven year history)
Each supplier followed same traceability requirement
Plant stopped if traceability system wasn’t on-line
Slide from Drew Richey.

## Slide 17: SCADA Architecture
Physical System
(sensors and actuators)
Wired or Wireless Connection
Programmable Logic Controller (PLC)
Network
Human-Machine Interface

## Slide 18: Physical System
Physical structure for the process
Embedded sensors that measure quantities such as pressure, temperature, flow, or density
Embedded actuators to control mechanisms such as solenoids, valves, or gates

## Slide 19: Wired (or wireless) Connection
Sends sensor signals to the controller
Sends controller commands to the actuators
Electrical communication between the controller and its physical interfaces

## Slide 20: Programmable Logic Controller
Digital Computer used on Automation
Input modules read data from sensors
User program decides what to do based on the input data
Output modules control actuators on the physical system

## Slide 21: What is inside a PLC?
Microcontroller - often older technologies
Network I/F
Physical System I/F
Memory
Program-
Ladder
logic

## Slide 22: Inside a PLC
Relays- outputs to actuators
Wire bridge for inputs
Battery- resilience

## Slide 23: Enterprise Network / Internet
Allows data exchange between the Programmable Logic Controllers and other computers
Enables supervisory software to query information from the plant
Communication follows a set of rules called Protocol
Output modules control actuators on the physical system

## Slide 24: Human Machine Interface
Graphical screens that consists of buttons, alarms, reports and trends about the process
Manages the physical process data
Provides a mechanism for user interaction and control

## Slide 25: Threats To SCADA
STUXNET
Iranian nuclear program attacked by nation state actor.
Maroochy
Australian water treatment plant attacked by insider.
Ukraine
Large scale blackout attack.
NY flood control dam attacked by Iranian hackers.

## Slide 26: How can we teach students to Defend these Systems?
First need to teach SCADA
  Unique system components - Cyber Physical Systems
  Unique programming - ladder logic
  Unique network protocols - Modbus, DNP3, etc.
  Legacy systems and components
Unique security requirements
  Availability, Integrity, Confidentiality versus Confidentiality, Integrity, Availability

## Slide 27: UAH SCADA Laboratory
Gas Pipeline
Water Treatment
Storage Tank
Real cyber vulnerabilities
Real physical impacts
Physical systems
Real actuators and sensors
Commercial PLC’s
Commercial Human Machine Interface (HMI) Software
Standardize networks

## Slide 28: Lab Options
Type | Description | Pros/Cons | # Students Served | Cost
Access to real systems | Co-op/intern or tour | Limited availability Real systems, real problems | One at a time for co-op/intern model. | $
SCADA Lab | Working SCADA commercial hard- ware & software | Limited physical system complexity Expensive | One student at time/system or teams. UAH has 3 systems. | $$$
PLC Lab | Commercial hard- ware & software | Limited physical system complexity Limited to one brand PLC Closed source | One student at time/system or teams. 20 PLC to a lab. | $$
OpenPLC | Bread boards + Arduino + PC | Limited physical system complexity Open source | Students purchase own kit and pair with PC. | $
Virtual SCADA | Matlab Simulink + OpenPLC (soft) | Model larger physical systems No kinetic effects | Available on PC via cloud. | $

## Slide 29: OpenPLC http://www.openplcproject.com
Runtime
multi-platform
soft PLC
Editor
PLC programation
Edit ladder logic (and 4 other languages)
Simulate and debug
GUI
build GUI’s
remote monitoring and control

## Slide 30: OPENPLC MODBUS Support Compared TO Commercial

## Slide 31: OpenPLC + ArDUINO+PC
OpenPLC runtime runs on PC.
Arduino provides Input/Output (IO): Analog and Digital
Inputs: buttons, sensors (various)
Outputs: LED, relays, speakers, etc.
Host only network from Virtual Box or lab network.

## Slide 32: OpenPLC + Raspberry PI
OpenPLC runtime runs on Raspberry PI.
Raspberry PI provides Input/Output (IO): Analog (low quality) and Digital
Inputs: buttons, sensors (various)
Outputs: LED, relays, speakers, etc.
Need monitor, mouse, keyboard to program.
Need lab network.

## Slide 33: Virtual SCADA Demo

## Slide 34: Refinery Distillation Column

## Slide 35: OPENPLC + Arduino Demo

## Slide 36: using a relay.
https://blog.siliconstraits.vn/relay-what-is-it-and-how-to-use-it/
Power (+)
Ground (-)
S = set (1) or not set (0)
Can connect to A/C or D/C on this side of relay.
Use 5V for this relay.

## Slide 37: using a relay.
https://blog.siliconstraits.vn/relay-what-is-it-and-how-to-use-it/
Normally open, Set = close
Normally closed, Set = open
Move this wire to change behavior
Don’t use both pins

## Slide 38: Where Can you get this Material?
http://clark.center
Search for SCADA
https://www.openplcproject.com/
Use Reference -> Creating your first project