## Slide 1: Session 6: Vulnerabilities
Tommy Morris
Professor, Electrical and Computer Engineering
Director, Center for Cybersecurity Research and Education
University of Alabama in Huntsville

## Slide 2: Network Attack Overview
Most SCADA networks have little to no authorization, making it easy for an attacker to access the network
Attacks often occur between the PLC and the HMI
  Called “Man in the Middle” (MitM) because attacker gets in middle of connection
Can be difficult to detect until it’s too late
  Information on screen may seem plausible to operator
Physical System
PLC
HMI
Actuator Data
Sensor Info
Attacker

## Slide 3: Interception/Reconnaissance
Attacker gains access to the network and can see information
Does not modify or block packets, just observes
Can learn system functions, commands, addresses, etc.
PLC
HMI
Command to turn on pump
Temperature sensor readings
Attacker

## Slide 4: Injection
Attacker sends their own commands or false data to the system
  Request data
  Turn system functions off
  Send fake sensor readings to HMI
With no authentication method, PLC and HMI won’t know it isn’t legitimate information
PLC
HMI
Attacker
Pipeline pressure is normal
Increase pump pressure

## Slide 5: Alteration
Attacker modifies the contents of existing packets
Order of events:
  Intercept legitimate packet
  Block the original from going through
  Modify packet
  Send changed packet
PLC
HMI
Warning: temp too high
Attacker
Temperature is normal

## Slide 6: Interruption
Attacker disrupts service between devices
Can overwhelm device with packets, such as ping requests
  Denial of Service (DoS) will be covered for next lab
In MitM, attacker can masquerade as other device
  Sender doesn’t realize it isn’t communicating with intended recipient
  Recipient never receives any data
PLC
HMI
Battery is low
Attacker
Notes: ARP (address resolution protocol) is used for routing
Attacker can “poison” the ARP cache of the sender, so it thinks the attacker is the one it wants to send to
This makes all packets from sender to intended recipient route through attacker
Discussed more in Lab Four

## Slide 7: Attacking the instructor
This exercise will introduce the concepts of Denial of Service (DoS) and Distributed Denial of Service (DDoS). Both techniques have the purpose of taking a target down by flooding the target with a large amount of data in a short time. The Low Orbit Ion Cannon (LOIC) will be used to perform the attacks for this exercise.
All students will target the heat exchanger PLC running on the lecturer’s computer. At first, only one student at a time will be allowed to attack the simulation (DoS). Then, all students in the class will perform the attack at the same time (DDoS).
Download LOIC from and extract the contents of the zip file on a folder.
Open LOIC.exe. On the main window, insert the target IP and click on Lock on.
Under “Attack options” type 502 on port, select Method “TCP”, type 1000 in Threads, and uncheck the “Wait for reply” option.
Click on “CHARGING MY LASER” and observe the results on the lecturer computer.

## Slide 8: Attacking the Instructor

## Slide 9: INJECTION Attacks
On this exercise students will perform an injection attack by fabricating messages with different settings and sending them to the target PLC. Students will use the Radzio! software to fabricate the messages. The target will be the heat exchanger PLC running on the lecturer’s computer. At first, only one student at a time will be allowed to attack the simulation. Then, all students in the class will perform the attack at the same time.
Download Radzio! from here and extract the contents of the zip file on a folder.
Open RMMS.exe. On the main window, go to Connection->Settings. Select Modbus TCP under “Protocol”, Register address starting from 0 under “Addressing convention”, and type the target PLC address on “IP address: “ field. Also, make sure that the TCP port is 502.

## Slide 10: INJECTION ATTACKS

## Slide 11: Injection Attacks
Click on File->New and Connection->Connect. On the new spreadsheet that appears, select Holding registers to view the PLC memory data.
Change the address to 1024
  The values displayed are the number1 and number2 fields for the advanced HMI problem.
  Double click on the first value and change it to be larger than the second number.
  The light should come one.

## Slide 12: INJECTION ATTACKS
Overwrite the memory used to store the enable blinking LED.
  ENABLE and DISABLE the LED from Radzio
Overwrite the memory used for the button input.
  Turn on the LED.
  Observe the behavior on the breadboard?
    Does the LED stay on?
  Observe the behavior in Radzio and on the HMI

## Slide 13
Radio Discovery < 24 hrs.
Infiltration < 30 days
Data Injection or Denial of Service Attack
Broken Feedback Control Loop
Human Machine Interface
Actual Pressure
Wireless Attack
Notes: This is an example attack enabled by wire link penetration with a Freewave industrial radio network.
For freewave case we can discovery active networks in a radius in less than 24 hours. We can penetrate these networks in < 30 days. Once inside denial of services, eaves dropping, and falsified network traffic injection possible.
Picture of gas pipeline shows results of denial of service attack. Inset shows actual pipeline pressure at 57.4 PSI, while HMI (larger picture ) 15 PSI. Very dangerous.
We can also inject false RTU responses to get similar results.
We have also successfully eavesdropped on communications.
The above work was done by an American undergraduate student who is a 4.0 Computer Engineering major and a National Merit Finalist. We have GREAT students! I am specifically interested in more UG funding. Great work, low price.
We are currently investigating command injection. We are developing a scanner find all connected masters, slaves, read out contents of all MODBUS registers, and build signature of each device.

## Slide 14: Wired Attack
RTU
Firewall/IDS
HMI
historian
Corporate Network
Control System Network
www
Penetrate Corporate Network
Penetrate Control System Network
  Inject false commands
  Inject false data
  Pollute historian
  Denial of service
How do adversaries penetrate the network?
  Many have little or no security
  Often there is no firewall between corporate and control system networks
  Advanced Persistent Threat – ala. Google Aurora

## Slide 15: Common Operational Network
DMZ
Enterprise Network
Control Room
Outstation
WWW

## Slide 16: Can malware infect the control room or outstation?
DMZ
Enterprise Network
Control Room
Outstation
WWW
Yes

## Slide 17: Can malware infect the control room or outstation?
DMZ
Enterprise Network
Control Room
Outstation
WWW
Yes

## Slide 18: How do adversaries penetrate the network?
Many networks no security or weak security.
  Default passwords.
  Poor security implementations.
Often there is no firewall between corporate and control system networks.
  Insider attack
Advanced Persistent Threat – ala. Google Aurora
  Adversary attacks specific target.
  Malware injection via SPAM
  Laptops corrupted while off corporate network
    at home, travelling, etc.
  Planted thumb drives containing malware

## Slide 19: Security Needs
Confidentiality
  Low priority for most control engineers.
  Needed to limit adversaries ability to collect pre-attack intelligence.
Integrity
  Authentication, Digital Signature
  Stop command and data injection.
Availability
  Avoid Denial of Service.
  Security solutions must not reduce control system availability.

## Slide 20: Security Needs
Traceability
  Support post incident analysis (forensics)
  Systems already capture control system data
  Need to capture network traffic
    Commands
    Responses
Intrusion Detection
  Detect network penetrations
  Stop denial of service, port scans
Survivability/Resilience
  Survive a cyber-attack
  Perhaps at reduced performance level (critical systems must survive)