## Slide 1: Waves and Channels
Unit: 1
Signaling

## Slide 2: Review
What are guard bands?
Types of multi access:
  FDMA
  TDMA
  CDMA -> “secret sauce”
ISL- intersymbol interference

## Slide 3: Objectives
Define how different waves propagate differently.
Establish the foundation for forward and reverse channels & duplex communications
Calculate the propagation of various types of radio waves

## Slide 4: Cellular Channels- Their Uses
Typically 4 channels dedicated
  Simplex Channels  What’s this?
2 Exchange Metadata
  Authentications
  Subscriber info
  Call parameters
2 Exchange real data
Control data needs to be exchanged before we can do data
Kind of like how FTP works

## Slide 7: Lifespans
Control channels are used very differently
How many channels do we assign to each?
  Depends on what we’re doing

## Slide 8: Back to Bandwidth
If I have the same bandwidth (say 3kHz) can I transfer the same amount of data?
What impacts this?
Are all protocols equally efficient?

## Slide 9: Examples
2G GSM .030 MHz .104mb/s 0.52
3G CDMA 1.2288MHz 3.072mb/s 0.125
4G LTE 20MHz 81.6mb/s 4.08
V.92 .004MHz 0.056mb/s 14.0
802.11g 20MHz 54mb/s 2.7
802.11ad 2160MHz 6756mb/s 3
mb/s vs MB/s

## Slide 10: Properties of Waves
Distance of the tower can impact things
Various frequencies act differently when transmitted

## Slide 11: How fast do waves travel?

## Slide 12: All waves travel at 300,000km/s
*technically -> 299,792,458 m/s
We can predict wavelength based on the frequency
So:
  300000 = frequency(Hz) x wavelength
  Cellphones – 800 MHz
  What’s the wavelength?

## Slide 13: Math!

## Slide 14: Wavelengths
FM Radio – 100Mhz, 3 m
Ka band satellite – 20GHz, 15mm
The frequencies are divided into various bands

## Slide 16: Signal Propagation
Free Space
  Basically, line of sight
  “Ideal” method of communicating
  Space ships, satellites, transmissions in “nothing”
Land
  This annoying planet gets in the way
  Antennas don’t broadcast in a ball

## Slide 17: How far can my wave theoretically go?
We need to know the power that’s received at the other end
Power is measured in watts
What’s this formula for:
Inverse square law
  Yes, I love Lucy is crossing the galaxy
  …but it’s a really weak signal
  Reception will be poor

## Slide 18: How far can my wave go?
*In an ideal world
Pr = Power received
d = distance from the source (radius)
Pt = power transmitted
Gt = gain of the antenna
Ae= area covered by the transmitter

## Slide 20: Going Further
*Assuming free space
Substitute Ae with receiving antenna gain (Gr) we get:
Stay calm, this isn’t that bad…
= power transmitted (watts)
d = distance in meters
= speed of light

## Slide 21: Propagation
I hope that I have line of sight LoS (or free space)
Reflection
  The radio wave bounces off something larger than the wave
  Like a planet or a building or the atmosphere
Diffraction
  A sharp edge bends the wave
  Edge of a wall
Scattering
  Something smaller than the wave gets in the way
  Like a tree

## Slide 23: Signal Processing
Hugely important concept
What’s the shortest/fastest distance between two points?
How many copies of a wave do I receive?
What if the signal reflects?
Flightradar24.com

## Slide 25: Waves have properties
Skywaves for example, love to reflect

## Slide 26: Ride the Waves
How far can you go?
FM vs AM are great examples
  AM: 535-1705kHz
  FM: 88 – 108 MHz
Basically: AM = big waves
      FM = little waves

## Slide 27: Ionosphere Reflection
AM Radio waves refract from the ionosphere
FM waves blast right through
Where do they go?
  AM: China
  FM: Mars
FM -> height is key, AM -> not really
Ionosphere is really good at refracting at night
AM
  Reduces power, directional antennas, shutdown

## Slide 28: Scales
Small-scale
  Signal variation/fading over a short distance
Large scale
  Signal variation/fading over a long distance
Diffraction & scattering -> small scale
Reflection -> large scale