## Slide 1: We all need to talk
Unit: 4
Signaling

## Slide 2: Recap
Cells are the radius covered by a BS
  Size vs capacity is important
Spectrum -> frequencies used to carry data
  Bandwidth -> range of frequencies used
  FM radio, example, 200kHz band
Bandwidth can carry the same amount of data
  No matter its frequency
  The protocol’s efficiency makes a difference
FCC regulates spectrum, etc.

## Slide 3: Objectives
Identify various methods of allowing multiple devices to communicate simultaneously
Define TDMA, FDMA, SDMA, and CDMA
Discuss strengths and weaknesses of each multi-access mechanism

## Slide 4: New Issue:
So we separate stuff out, that’s great…
We have lots of cell phones
How can we all use them at the same time?
Consider a walky-talky:
  Can you carry on multiple conversations at once?
Enter the need: multiplexing
  Let’s us carry multiple signals over a single shared medium
  Can be a cable or a radio wave

## Slide 5: Multiplexing: FDMA
And oldie but a goodie!!
Frequency Division Multiple Access
  Basically: divide up our frequency into small pieces for each user
  These are called channels
Pros: easy and works great!
Cons: Crosstalk
1st Generation technology
Original analog cell phones

## Slide 7: Multiplexing: TDMA
FDMA sucks… One user can hog the signal
Solution: put them on a timer!
Time Division Multiple Access
2G technology here
  Essentially: digital voice
Examples: GSM
Used a lot in satellites
Sync Overhead
Collisions

## Slide 9: CDMA- Sound Familiar?
Code Division Multiple Access
Mix a not-so-secret code in for each user
  Encodes raw data with code
  Transmits, removes code at other end
Uses a wider frequency
Now we’re talking 3G technology
Scalability
  Limited by the number of codes you can come up with
  How fast can you code/decode your data
  Near/Far

## Slide 12: Space Division Multiple Access
I’m pointing my signal at YOU
  And only you…
Basically, directional antennas on BS and MS
  Can reuse channels
  No interference
  High quality signal
Problems
  Tech is fairly new
  How many antennas can you hang from a tower?

## Slide 13
MS1
MS2
MS3
BS
Beam 1
Beam 2
Beam 3

## Slide 14: Big Advantages of each:
FDMA
  Really easy
TDMA
  Flexible growth
CDMA
  Nearly unlimited growth?
SDMA
  Infinite capacity, pair with CDMA for extra goodness

## Slide 15: Problems
FDMA
  Wastes spectrum, guard bands, no changing frequencies
TDMA
  Needs guard space + time sync issues
CDMA
  Requires signal processing + power levels
SDMA
  Mobile clients are tough to handle

## Slide 16: Where do we use them?
FDMA
  Radio & TV
TDMA
  Mostly GSM, 2G & 3G
CDMA
  2.5 and 3G Communications
OFDM
  The 4G’s
SDMA
  Satellites