## Slide 1: Introduction
Unit: 4
Modulation

## Slide 2: Objectives
Define and compute sampling rate for digital signaling
Compare sample rates for common audio sources and observe how sample rates impact digital signal quality

## Slide 4: Sampling Rate
We have to take samples of a signal and store it somehow
Big deal in the audio world
Also called: sampling frequency
Measured in hertz! (cycles per second)
Bandwidth: what’s the range
Around 40000 Hz may be familiar to audio folks (40 kHz)
  Why?

## Slide 5: Nyquist Principle
If our frequency of sampling is > two times maximum frequency of the sample…
We avoid aliasing and have a “perfect” reproduction
Why is audio around 40kHz then?
We can only hear 20,000Hz, so double it and we’re set

## Slide 6: Common Sampling Rates
8,000 Hz, analog phones, walkey talkeys
16,000 Hz, common for VoIP stuff
44,100 Hz, audio CD’s (we can thank Sony for this)
48,000 Hz, Consumer video stuff, digital TV, DVD
96,000 Hz, Blu-ray, HD DVD
Tidbit: most human conversation is in the 5Hz – 4kHz range
  Hence we sample it at 8 kHz

## Slide 7: Real Hardware Sampling
Fancy expensive radios
  Ettus B200’s: 61.44 mHz (61.44 million samples per-second)
  This is a lot
Wifi typically rolls with 20 MS
Sometimes we need to re-sample
  Convert signals sampled at one rate to another
  Example: taking in FM radio and passing it you your sound card
  Sound cards -> typically 48ksps

## Slide 8: Other Sampling Stuff
GNU Radio will sometimes label sampling rate as:
  Samples per Second (ksps)
  Which isn’t “official” but it makes more sense than saying:
    I sampled the 15,000 Hz signal at 30,000 Hz
    Instead…
    I sampled the 15,000 Hz signal at 30,000 samples per second (or 30 ksps)
Other trickyness
  Since this is all defined in software, we’re technically simulating the sampling, so technically it’s all fake
  Real world: if you’re not careful, you may max out your CPU generating samples

## Slide 9: Concepts within
Graphs- pie chart, bar graph, etc
Blocks- actual signal processing (usually C++/Python backend)
Ports connect blocks together
Source: Block’s w/ only output
Sink: block with only input