## Slide 1: GSM Frames
Unit: 1
GSM

## Slide 2: Review
What are the units of cellular RF divided up into?
What are the individual time slots of GSM’s TDMA called?
  How many are there?
What’s the first time slot used for?
What were combinations?

## Slide 3: Combination V
  FCCH: Frequency Correction Channel
  Zeros!
  SCH: Synchronization Control Channel
  Timing
  BCCH: Broadcast Control Channel
  What’s here?

## Slide 4: New Channels
FCCH
SCCH
CCCH- Common Control Channel
  Basically… paging your phone
  Your phone lives a boring life...
    Just listens to CCCH
Replies from the phone: RACH
  Phones reply to a CCCH request
  Phones can also initiate connections with a RACH

## Slide 5: Order of Operations
Phone turns on (or leaves airplane mode)
FCCH – finds a seemingly usable frequency
SCH- Where is the network currently at, timing wise?
BCCH- Are you my mother?
Boom, you’re connected
Sit and contemplate life
CCCH- Hey, wake up and do something!
Mobile to BTS: RACH- acknowledged

## Slide 6: Last Piece of Combo V
SDCCH- Standalone Dedicated Control Channel
Also exists in Combo VII
CCCH’s really just wake up the device
SDCCH’s set stuff up
  Sync channels for:
    Call
    SMS
    Location Updates
    More stuff
Basically prepares us for a TCH

## Slide 7: TCH- Traffic Channel
Not exceptionally fast…
  Roughly 13kb/s
  Uses GSM codec though, not IP
Primarily for voice or GPRS data
Can also do a FACCH- Fast Associated Control Channel
  Used for call metadata: caller hung up
Uses the Stealing Flags

## Slide 8: Others… SACCH
Slow Associated Control Channel
Handles real time radio management stuff
  Timing information/corrections
  Power commands
  Receives/reports power info

## Slide 9: Layer 3 goodies
Pieces inside of Layer 3:
  Radio Resource- Manages dedicated channels
    Handle physical/logical channels
    Paging handsets
    Create the beacon
    Basically describe the physical layout of the network
  Mobility Management- Handling MS
  Call Control or Short Message Service- Processing Calls

## Slide 10: Layer 3 goodies
Pieces inside of Layer 3:
  Radio Resource- Manages dedicated channels
  Mobility Management- Handling MS
    Who on our network deals with that MS?
    Authenticate users
    Basically: user identities/authentication
  Call Control or Short Message Service- Processing Calls

## Slide 11: Layer 3 goodies

## Slide 12: What kind of channels can we play with?
Really, phone/data types
LUR- Location Update Request
MOC- Mobile Originated Call
MTC- Mobile Terminated Call
MO-SMS- Mobile Originated SMS
MT-SMS- Mobile Terminated SMS
EmergencyCall- Emergency MOC