## Slide 1: Identifying a Network
Unit: 2
Networking

## Slide 2: Review
What does your phone spend life doing?
RACH- Random Access Channel
  What problems can occur with randomly sending data?
Does everything we talk about only apply to GSM?

## Slide 3: How to pick your network!
Task at hand:
  You’ve picked up a BCCH
  It’s full of information
  Now what?

## Slide 4: Identity Stuff: MCC
Mobile Country Code
3 digit number assigned by ITU
  International Telecommunication Union
Actually multiple parts
USA -> 310 primarily
  A few things on 311
  A couple on 316
Test -> 001
!!!This is different from E.164 (Phone numbers)
0- Test Networks
2- Europe
3- North America
4- Asia & Middle East
5- Oceania
6- Africa
7- South & Central America
9- Other stuff

## Slide 5: Identity Stuff: MNC
Mobile Network Code
2 or 3 digits
Assigned by national regulator
01 -> Test Networks
Weirdness:
The US uses 3 digit MNC’s
  The rest of the world uses 2 digits
  Therefore: International US MNC’s end with 0 (roaming)
The US has 7 MCC’s
  Potential for 7 duplicate MNC’s in the US

## Slide 6: Examples
United States, 310
  150, 170, 560 AT&T + more
  026, 260, 580 T-Mobile
Verizon has like 40
Lookup your network IDs:
  mcc-mnc.com
Some CDMA networks don’t use MCC/MNC’s

## Slide 7: LAC
Location Area Codes
16 bits of goodness (0xFFxx are “reserved”)
Number to ID the paging area of the BTS
Whenever your MS moves, it updates its LAC
  Aka: hands off to another BTS

## Slide 8: CI
Cell ID
16 more bits of fun!
Unique for every BTS in the network

## Slide 9: More fun! BSIC
Base Station Identity Code
6 bits, broken into two pieces
  NCC- Network Color Code
    Unique for each network
    Values of 0 to 7
    Assigned by a regulator of some sort
  BCC- Base Station Color Code
    Unique to adjacent BTS
This is really just important for folks using the same ARFCN

## Slide 10: Where do we find MCC + MNCs?

## Slide 11: SIM Cards!
Subscriber Identity Module
Circuit that stores many things!
For now, it stores an IMSI
  International Mobile Subscriber Identity
  14-15 digit number that ID’s the subscriber
  Basically, your username

## Slide 12: IMSI
They’re a big deal
You don’t want to disclose your IMSI
You can’t <usually> “look up” your IMSI
Made up of: MCC + MNC + MSIN
MSIN: Mobile Subscription Identification Number
  So:
  310150123456789 would be: 310 150 123456789
  MCC MNC MSIN
You don’t want others to know your IMSI…

## Slide 13: GSM’s Fix
You don’t want others to know your IMSI…
So, you usually use a TMSI
Temporary Mobile Subscriber Identity
32 bit number to ID you on the network
Helps you to be sort of anonymous <- LOL

## Slide 14: Other ID’s: IMEI
International Mobile Equipment Identity
15 digit that ID’s the handset
Sort of a MAC address
GSM doesn’t really use IMEI’s
  Except for theft
CDMA uses a similar thing: MEID, Mobile Equipment Identifier
You may also see ESN
  We’re getting rid of these, not big enough

## Slide 15: Last One: MSISDN
Mobile Subscriber Integrated Services Digital Number
Any idea what this is?

## Slide 16: MSISDN
It’s the handset’s phone number! (per E.164)
Fun Fact:
  Handsets are mostly unaware of their MSISDN
  MSISDN to IMSI association is only on the network/BTS
    Note: MSISDN to IMSI… Not TMSIS!
  Never: MSISDN to IMEI