## Slide 1: SIM Fun!
Unit: 2
Networking

## Slide 2: Review
What’s so cool about SS7?

## Slide 3: Subscriber Identity Module
Stores what value?

## Slide 4: Things SIMs store
…Can store
Address book
SMS messages
Apps

## Slide 5: What are they really?
Universal Integrated Circuit Card (UICC)
Generally embedded in PVC
  The plastic ones suck
  I have plastic ones
Various form factors

## Slide 6: SIM Forms
Standard: size of credit card
Mini: about an inch tall
Micro: a little over ½ inch tall
Nano: a wee but under a ½ inch tall
Embedded: soldered into the phone

## Slide 7: Size isn’t that big of a deal: why?

## Slide 8: SIM Info
Usually ID’d by a serial number of sorts
  Prefer not to use IMSI
  ICCID- Integrated Circuit Card Identifier
ICCID Made of:
  89 -> they all start with 89, just because
  Country code (like 1)…
  Issuer ID (usually 1-4 digits)
  Account ID
  Check digit
Usually printed on the SIM

## Slide 9: Java Card?
Allow Java apps to run from SIM
Not used in the US
Developing countries

## Slide 10: MNC’s
Really important
Standard SIMs have room for 33 MNC’s
Others can hold up to 80MNC’s
Important for roaming
  Going to roam? You may get a new SIM
What’s a cheap way to roam to <non-US> places?

## Slide 11: Auth Key
Called the ‘Ki’
Each is unique
Programmed by network provider
  AuC– stores it
Write-Once Write-Only area of memory
  Similar to ROM
128 bit value

## Slide 12: Cool Ki Stuff
Remember, a SIM is a computer
Can’t read the Ki
Signs data w/Ki though

## Slide 13: Auth Procedures: SUCKS
Handset starts up
  Gets IMSI from SIM, hands to BTS
Network looks up the IMSI’s Ki
Network generates rand, signs it with Ki, returns:
  Signed Response I -32 bit number
  Encryption Key -64 bit key
Sends rand to the phone
  Phone passes rand to the SIM
  SIM returns a signed number
Phone returns the signed number
  It should match what the network created