## Slide 1: Kismet
Unit: 5
Wireless

## Slide 2: Review
Terrible Security Methods
  Hiding SSID
    Probes
    Association Request
  MAC Address Filters
    Spoofable
802.11 Frames
  Beacon -> sent by AP, advertisement
  Probe -> from clients,

## Slide 3: AP Sensitivity
Measurement of overall signal strength
Confusing/backwards sounding measurements
dBm for your AP
  Closer to zero the better
    -20 dBm -> VERY close to the AP
    -90 dBm -> pretty far away from the AP

## Slide 4: Sensitivity
Typical values are -80 dBm to -90 dBm
Each 3 dBm change represents doubling of sensitivity
  High end cards get as much as -93 to -97 dBm
Convert mW to dBm:

## Slide 5: A New Contender Enters: Kismet
What is it?
  Network scanner
  Sniffer
  Wireless IDS
Has cool plugins
  Bluetooth
  SDR
  Zigbee

## Slide 6: Kismet as IDS
Not going to talk about scanner/sniffer
  I’d rather use aerodump-ng for that
    …personally
  Makes a good/quick visual of what’s going on
IDS
  Best as a stationary device
  Moving around/war driving: confusion for IDS
Can actually integrate with Snorts

## Slide 7: Things Kismet Will Look For
APSpoof -> We config a list of legit BSSID’s for an SSID. Any new MAC’s, spoofer!
BSSTimestamp -> does the beacon from this BSSID match the timestamp of others with the same SSID?
ChanChange -> Generally a BSSID won’t channel hop, this is hit or miss
CryptDrop -> Same SSID, less crypto

## Slide 8: More
DeAuthFlood/BCastDiscon -> watches for fake disassociate/death frames
LongSSID
  You can actually crash some OS/Hardware/Drivers by violating the spec, 32 bytes for an SSID
ProbeNoJoin
  Send out probe packets for a valid network but never join it

## Slide 9: Playing with Kismet
Fun GUI with lots of visuals
BSSID’s
Channel/spectrum use
  How crowded is this place
Signal strength

## Slide 10: Kismet/Wireshark
Again, just watching/displaying frames as seen
We can see Kismet distinguishes
  Probes vs Beacons
  Both legit ways to discover a network
Play with Wireshark?

## Slide 11: Next Time…
The glories of WEP
  And the RC4 stream cipher
  And why it’s the worst thing ever