## Slide 1: WPA/WPA2
Unit: 5
Wireless

## Slide 2: WPA: A New Hope
Wi-Fi Protected Access
“WEP is terrible, let’s find a good alternative”
Came about in 2003

## Slide 3: What made WEP bad?

## Slide 4: Haters Gonna Hate
WEP’s problems:
Key Size
  The key is too small
  Most of the key is static -> user entered portion
  Fixed size
  Not much for generating dynamic keys
Reuse of keys
  Encryption is based on user key
  We then all use that key

## Slide 5: Things to improve
Make keys bigger
Change keys more often
Don’t fix the size
Don’t force it to be hex

## Slide 6: TKIP
Temporal Key Integrity Protocol
Wild idea: change the key used for encryption!
TKIP does this per-packet
A new 128-bit key is generated for each packet
Therefore: not any longer than WEP
  But it changes
Purpose: fix WEP security via a firmware update

## Slide 7: Authentication?
More complicated process
Creates a pairwise master key (PMK)
  Computed from PSK and SSID
Client uses PMK, encrypts exchange of temporary key
  Called pairwise transient key (PTK)
Keys changed every time a client connects
  Therefore: you and I can’t see each other’s traffic

## Slide 8: Auth/Encryption
The final keys are generated from:
  PMK
  Client generated random number
  AP generated random number
  MAC address of client + AP
Pretty good key

## Slide 9: Good key?
Lots of info go into the key
Cracking it is still possible- mostly brute force
  Still using RC4
Problem with WPA
  Still ends up with relatively small key (128-bit)
  TKIP is good, not awesome
What’s better?
  WPA2

## Slide 10: WPA2
WPA brings in TKIP, pretty good
  Cracking is (mostly) brute force
  TKIP’s flaws aren’t that exploitable -> It’s RC4 that is
Even better: AES
  Advanced Encryption Standard
  Really good encryption!
  Brutal on crappy CPU’s
So, the problem with WEP -> WPA transition?
  The hardware was “not ideal

## Slide 11: WPA2 -> The better choice!
CPU’s are much cheaper now
WPA2 give us the option:
  TKIP
  AES
WPA/WPA2 (especially WPA2)
  Really only brute force methods work

## Slide 12: What we need?
We need to passively listen
Specifically:
  Clients joiining/leaving the network
You can be very stealthy with this
  As in: impossible to detect
  WEP -> detectable, sort of
What do you need? Airmon & airodump!

## Slide 13: Sniffing
Fire up airmon
airodump-ng
  --channel
  --bssid
  --write
  mon0

## Slide 14: Minimum frames may be needed
We don’t feel like waiting too long
aireplay-ng –deauth 10 –a BSSID –c CLIENT mon0

## Slide 15: Cows are cool
coWPAtty
Fairly fast/efficient WPA cracker
One WPA/WPA2 biggie: keys are hashed 4096 times
  We’ll want to use a wordlist
cowpatty –f <wordlist> -s SSID –r captureFile
Check /usr/share/wordlists/fasttrack.txt