## Slide 1: Cellphone Stuff!

## Slide 2: Where are we going?
Working towards a working BTS
  Base Transceiver Station
Start out small, work our way up to it
Primarily GSM stuff
  Zero CDMA (Like Verizon and Sprint)
  GSM- Global System for Mobile

## Slide 3: What will we have?
OpenBTS- software implementation of cell infrastructure
  Most of The Big Guys have really complicated infrastructure
  OpenBTS tries to standardize it as much as possible
Talk the talk?
  We’ll have a 2G network
    GSM
    Voice and SMS
  OpenBTS can also do “2.5G”
    GPRS Data
    Tough to do in a VM

## Slide 4: ARFCN
Absolute Radio-Frequency Channel Number
How is cellular spectrum actually divided up?
Kind of like 802.11 -> they overlap
Each cellular band is divided up
  Don’t want to overlap
  Licensed by FCC

## Slide 5: ARFCN’s
Adjacent ARFCN’s overlap frequencies ^^ This is wifi, but still…
Each band (channel) is 270.833kHz of bandwidth
Each pair has fixed up/down link frequencies

## Slide 6: Legality?
So technically this isn’t legal to do
Spectrum
  850,900, 1800, and 1900MHz is where GSM lives
  Not really supposed to use those
Rules of engagement:
  Not connecting antennas
  No amplifiers
  Total network range will be about 10 feet

## Slide 7: Duplex Communication
Up/Down at the same time: FDMA
Multiple phones -> TDMA
We need two different frequencies!
  And technically, licenses for each

## Slide 8: Frequency Bands
Three primary regions
  1 Europe and Africa
  2 Americas
  3 Asia
Quad Band Handsets?
  ”World Phones”
  Support 850, 900, 1800, 1900 mHz

## Slide 9: What ARFCN are you using?
iOS, dial: *3001 # 12345 # *
Android dial *#0011#

## Slide 10: SMS FTW
Tough to max out system capacity
Around 1800 per ARFCN per minute
SMS doesn’t care about data loss so much
  Retransmission!

## Slide 11: What’s inside GSM
Essentially an OSI Model…
Only 3 layers of fun
L3- communication Management Layer
L2- Data Link Layer
L1- Physical Layer

## Slide 12: Layer 1: Timing is Everything
We’re using 8-way TDMA
Time slots are actually called ‘physical channels’
How many “full-rate” calls can we handle over 8 physical channels?
Question: How much voice data do you lose?
What would half-rate do for us?