## Slide 1: Cellphone Stuff!

## Slide 2: Review
What are the units of cellular RF divided up into?
What frequencies do cellular devices tend to live on?

## Slide 3: Frequency Bands
Three primary regions
  1 Europe and Africa
  2 Americas
  3 Asia
Quad Band Handsets?
  ”World Phones”
  Support 850, 900, 1800, 1900 mHz

## Slide 4: Layer 1: Timing is Everything
We’re using 8-way TDMA
Time slots are actually called ‘physical channels’
How many “full-rate” calls can we handle over 8 physical channels?
Question: How much voice data do you lose?
What would half-rate do for us?

## Slide 5: Physical Channels
What can we do on a channel?
  Remember: T0 through T7 = 8 channels
Restricted to certain things… called Combinations
Combination V: The Beacon
  Reserved and always sent at T0
Combination I: full rate traffic
  Used for voice or GPRS (slow data)
Combination VII: SMS
  (and management sort of stuff)

## Slide 6: Combinations: The Breakdown
Combinations are broken down into “logical channels”
Logical vs Physical channel?
  Physical channel = single time slot
  Logical Channel = data carried in physical channel
It takes about 4.62ms to send a burst on all 8 physical channels
Every physical channel is divided into 50 burst periods
  What’s a burst?
  Lasts for about 15/26 ms

## Slide 7: Regular Bursts
We’re going deep
Likely deeper than you’ve gone in networking…
We’re going to the bit level

## Slide 8: Regular Bursts
Basically raw packets, sort of
Fast flying: 1 burst every 576.9μs
What exists here?
164.5 bits of data

## Slide 9: Regular Bursts
What exists here?
  2X 3 tail bits
  True start of the burst (the guard really isn’t a start, 8.25 bits??)
  Tail bits:
    Electronics need a bit of time to come alive
    These bits are literally for your transmitter to have time to power up

## Slide 10: Regular Bursts
What exists here?
  57 bits of data
  Usually going to be… voice??
  Can also be a FAACH
    Fast Associated Control Channel – we’ll come back to a FAACH

## Slide 11: Regular Bursts
Basically raw packets, sort of
Fast flying, remember: 1 burst every 576.9μs
What exists here?
  1 bit of signage
  Stealing Flag
  Indicates what type of data we just received in the previous 57 bits
  Tells us if this is a Traffic Channel or a FACCH.

## Slide 12: Regular Bursts
Basically raw packets, sort of
Fast flying, remember: 1 burst every 576.9μs
What exists here?
  26 bits for the Training Sequence
  Clock synchronization & differentiation!
  There’s 8 different options that can fit here
  This is how your MS differs BTS’s– the TS is different for each BTS

## Slide 13: Regular Bursts
Basically raw packets, sort of
Fast flying, remember: 1 burst every 576.9μs
What exists here?
  Another data indicator- SF
  57 bits of data
  3 bits– give time to turn down the transmitter
  ”wait for 8.25 bits”

## Slide 14: That’s enough burst talk
That’s as “deep” as we’ll go into a GSM packet today…
Which… is pretty deep actually...
Fun fact, with the guard bands, the margin of timing error is about:
  31μs (.031ms)

## Slide 15: Things are tricky
Some data is too big for a burst
They become interleaved over multiple burst periods

## Slide 16: Logical Channels
We’ve gone down to the burst…
Let’s go up a bit
Still living at L1 of GSM

## Slide 17: Identity is important
Your MS needs to know it’s locking onto the right BTS
Some things are unique to T0 & Combination V
  FCCH: Frequency Correction Channel
    Transmit all zeros!
    Makes a solid tone when demodulated- 67.7 kHz above center
    MS uses this to lock on its oscillator
  SCH: Synchronization Control Channel
    Tells us where we are in this whole timing mess
    Eg: T0 C1
  BCCH: Broadcast Control Channel
    Important info! Cell identity, how to access it, what ARFCNs to use, how to register, and:
    Do you take emergency calls?
    MNC, LAC, neighbor ARFCNs