## Slide 1: Receiving Signals
More GNU Radio

## Slide 2: Review
What’s the purpose of a sine wave?
Why do we need modulation?
What were our two types?

## Slide 3: Today’s Fun
Capture some raw RF
Some disclaimers: capturing is easy
  It does tend to take a lot of space
  About 2,400,000 samples per second
Actual processing disclaimers
  VM vs raw CPU
  Won’t sound pretty

## Slide 4: Basics First
Let’s capture a signal and write it to file
What frequency should we center on?
What sample rate would we want?

## Slide 5: Rates
This gets tricky
We want to sample at a rate our hardware likes
Can go lower on occasion, can never go higher
  Can’t ask for more data than what’s being produced!
Can never use throttles
  Two clock issues
  Keep timing consistent
These particular [crappy] radios
  Around 2-2.4 megasamples

## Slide 6: Taking in FM Radio: Resampling
2M samples/second is obscene
Interpolation
  Discrete math for the win!
  Basically: average out the signal
Decimation
  downsampling
Convert one sample rate to another that’s related
  We can aim to produce around 500k

## Slide 7: Low Pass Filter
Filter out junk we don’t want!
We have a given “expected” band
  Basically: what’s our bandwidth?
Given the data, filter out what appears to be background noise
Sample Rate: What’s the rate we’re processing?
Cutoff Frequency: How wide of a band are we looking at?

## Slide 8: WBFM Receive
We’re cheating a little…
We have now cleaned out our signal
  We’re down to a [fairly] basic sine wave
We need to demodulate the data to something useful
Quadrature rate: 500k
Decimation: 1/100th, so 50!

## Slide 9: Finally…
Audio sink
May need to re-sample again

## Slide 10: Issues…
Especially with VMs
Audio buffering
Excessive processing