## Slide 1: We all need to talk

## Slide 2: Recap
Cells are the radius covered by a BS
  Size vs capacity is important
Spectrum -> frequencies used to carry data
  Bandwidth -> range of frequencies used
  FM radio, example, 200kHz band
  How much “bandwidth” does it really need?
Bandwidth can carry the same amount of data
  No matter its frequency
  The protocol’s efficiency makes a difference
FCC regulates spectrum, etc

## Slide 3: Transmitting
One way transmissions are easy
  FM/AM radio for example
Two way isn’t that hard either

## Slide 4: New Issue:
So we separate stuff out, that’s great…
We have lots of cell phones
How can we all use them at the same time?
Consider a walky-talky:
  Can you carry on multiple conversations at once?
Enter the need: multiplexing
  Let’s us carry multiple signals over a single shared medium
  Can be a cable or a radio wave

## Slide 5: Multiplexing: FDMA
And oldie but a goodie!!
Frequency Division Multiple Access
  Basically: divide up our frequency into small pieces for each user
  These are called channels
Pros: easy and works great!
Crosstalk
1st Generation technology
Original analog cell phones
1
2
3
…
n
Total bandwidth
4

## Slide 6
User 1
Frequency 2
User 2
Base Station
Frequency n
User n
…
…
Mobile Stations
User 1
User 2
User n
…
Frequency
Time

## Slide 7: Multiplexing: TDMA
FDMA sucks… One user can hog the signal
Solution: put them on a timer!
Time Division Multiple Access
2G technology here
  Essentially: digital voice
Examples: GSM
Used a lot in satellites
Sync Overhead
Collisions

## Slide 8
Time 1
Time 2
Time n
…
User 1
User 2
User n
…
Mobile Stations

## Slide 9: CDMA- Sound Familiar?
Code Division Multiple Access
Mix a not-so-secret sauce in for each user
  Encodes raw data with code
  Transmits, removes sauce at other end
Uses a wider frequency
Now we’re talking 3G technology
Scalability
  Limited by the number of codes you can come up with
  How fast can you sauce/unsauce your data
  Near/Far

## Slide 10
Information bits
Code at transmitting end
Transmitted signal
Received signal
Code at receiving end
Decoded signal
at the receiver
Time
Time
Time
Time
Time
Time

## Slide 11
Time
User n
Code
User 1
User 2
.
.
.
Frequency

## Slide 12: Intersymbol Interference
Problem we run into: the world isn’t flat
  People put up these stupid buildings
Radio waves bounce off these, can’t take a straight path
  Data arrives out of order
  Called Intersymbol Interference

## Slide 13: Cellular Infrastructure
Many base stations exist, each in their own cell
A Base Station Controller coordinates the Base Stations
Mobile Switching Centers connect to the Base Station Controllers
MSC’s then connect to….
  PSTN- Public Switched Telephone Network -> Phone calls!
  Internet

## Slide 14: Mobile Switching Centers
MSC’s handle some important info
Home Location Register
  Mobile device's HLR is in their billing area
  Where does your number originate from
  All incoming calls are directed here
    May get redirected
Visitor Location Register
  Mobile devices roaming connect here
  Remember cell phone roaming?

## Slide 15: Provoking Thoughts
In an airplane, how well would these work:
  Walky-talky?
  Satellite Phone?
  Cell Phone?
What happens to cell signal when on a long metal bridge?

## Slide 16: Cellular Channels- Their Uses
Typically 4 channels dedicated
  Simplex Channels  What’s this?
2 Exchange Metadata
  Authentications
  Subscriber info
  Call parameters
2 Exchange real data
Control data needs to be exchanged before we can do data
Kind of like how FTP works

## Slide 17: Math
If a total of 33 MHz of bandwidth is allocated to a particular cellular telephone system which uses two 25 kHz simplex channels to provide full duplex voice channels, compute the number of simultaneous calls that can be supported per cell if a system uses:
  FDMA
  TDMA with 8-way time multiplexing

## Slide 18
Base Station
Forward (downlink) control channel
Mobile Station
Forward (downlink) traffic channel
Reverse (uplink) traffic channel
Reverse (uplink) control channel

## Slide 19
BS
MS
1. Need to establish path
2. Frequency/time slot/code assigned
(FDMA/TDMA/CDMA)
3. Control information Acknowledgement
4. Start communication
BS
MS
2. Ready to establish a path
3. Use frequency/time slot/code
(FDMA/TDMA/CDMA)
4. Ready for communication
5. Start communication
1. Call for MS # pending
Incoming Call
Outgoing Call

## Slide 20: Lifespans
Control channels are used very differently
How many channels do we assign to each?
  Depends on what we’re doing

## Slide 21: Back to Bandwidth
If I have the same bandwidth (say 3kHz) can I transfer the same amount of data?
What impacts this?
Are all protocols equally efficient?

## Slide 22: Examples
2G GSM .030 MHz .104mb/s 0.52
3G CDMA 1.2288MHz 3.072mb/s 0.125
4G LTE 20MHz 81.6mb/s 4.08
V.92 .004MHz 0.056mb/s 14.0
802.11g 20MHz 54mb/s 2.7
802.11ad 2160MHz 6756mb/s 3
mb/s vs MB/s

## Slide 23: Properties of Waves
Distance of the tower can impact things
Various frequencies act differently when transmitted
Earth
Ground wave
Space wave
Receiver
Transmitter
Ionosphere (80 - 720 km)
Mesosphere (50 - 80 km)
Stratosphere (12 - 50 km)
Troposphere (0 - 12 km)