## Slide 1: Waves and Channels

## Slide 2: Review
Multiplexing
  Allowing multiple entities to talk
  Share one piece of spectrum
Types of multi access:
  FDMA
  TDMA
  CDMA
ISL- intersymbol interference

## Slide 3: Cellular Channels- Their Uses
Typically 4 channels dedicated
  Simplex Channels  What’s this?
2 Exchange Metadata
  Authentications
  Subscriber info
  Call parameters
2 Exchange real data
Control data needs to be exchanged before we can do data
Kind of like how FTP works

## Slide 4
Base Station
Forward (downlink) control channel
Mobile Station
Forward (downlink) traffic channel
Reverse (uplink) traffic channel
Reverse (uplink) control channel

## Slide 5
BS
MS
1. Need to establish path
2. Frequency/time slot/code assigned
(FDMA/TDMA/CDMA)
3. Control information Acknowledgement
4. Start communication
BS
MS
2. Ready to establish a path
3. Use frequency/time slot/code
(FDMA/TDMA/CDMA)
4. Ready for communication
5. Start communication
1. Call for MS # pending
Incoming Call
Outgoing Call

## Slide 6: Lifespans
Control channels are used very differently
How many channels do we assign to each?
  Depends on what we’re doing

## Slide 7: Back to Bandwidth
If I have the same bandwidth (say 3kHz) can I transfer the same amount of data?
What impacts this?
Are all protocols equally efficient?

## Slide 8: Examples
2G GSM .030 MHz .104mb/s 0.52
3G CDMA 1.2288MHz 3.072mb/s 0.125
4G LTE 20MHz 81.6mb/s 4.08
V.92 .004MHz 0.056mb/s 14.0
802.11g 20MHz 54mb/s 2.7
802.11ad 2160MHz 6756mb/s 3
mb/s vs MB/s

## Slide 9: Properties of Waves
Distance of the tower can impact things
Various frequencies act differently when transmitted
Earth
Ground wave
Space wave
Receiver
Transmitter
Ionosphere (80 - 720 km)
Mesosphere (50 - 80 km)
Stratosphere (12 - 50 km)
Troposphere (0 - 12 km)

## Slide 10: How fast do waves travel?

## Slide 11: All waves travel at 300,000km/s
*technically -> 299,792,458 m/s
We can predict wavelength based on the frequency
So:
  300000 = frequency x wavelength
  Cellphones – 800 MHz
  What’s the wavelength?

## Slide 12: All waves travel at 300,000km/s
We can predict wavelength based on the frequency
So:
  300000 = frequency x wavelength
  Cellphones – 800 MHz
  What’s the wavelength?
  800 MHz = 800,000,000 Hz

## Slide 13: All waves travel at 300,000km/s
We can predict wavelength based on the frequency
So:
  300000 = frequency x wavelength
  Cellphones – 800 MHz
  What’s the wavelength?
  800 MHz = 800,000,000 Hz
  300,000 = 800,000,000 x ?

## Slide 14: All waves travel at 300,000km/s
We can predict wavelength based on the frequency
So:
  300000 = frequency x wavelength
  Cellphones – 800 MHz
  What’s the wavelength?
  800 MHz = 800,000,000 Hz
  300,000 = 800,000,000 x ?
  300,000/800,000,000 = ?
  = 37.5cm

## Slide 15: Wavelengths
FM Radio – 100Mhz, 3 m
Ka band satellite – 20GHz, 15mm
The frequencies are divided into various bands

## Slide 16
Classification Band | Initials | Frequency Range | Characteristics
Extremely low | ELF | < 300 Hz | Ground wave
Infra low | ILF | 300 Hz - 3 kHz | 
Very low | VLF | 3 kHz - 30 kHz | 
Low | LF | 30 kHz - 300 kHz | 
Medium | MF | 300 kHz - 3 MHz | Ground/Sky wave
High | HF | 3 MHz - 30 MHz | Sky wave
Very high | VHF | 30 MHz - 300 MHz | Space wave
Ultra high | UHF | 300 MHz - 3 GHz | 
Super high | SHF | 3 GHz - 30 GHz | 
Extremely high | EHF | 30 GHz - 300 GHz | 
Tremendously high | THF | 300 GHz - 3000 GHz | 

## Slide 17: Signal Propagation
Free Space
  Basically, line of sight
  “Ideal” method of communicating
  Space ships, satellites, transmissions in “nothing”
Land
  This annoying planet gets in the way
  Antennas don’t broadcast in a ball

## Slide 18: How far can my wave theoretically go?
We need to know the power that’s received at the other end
Power is measured in watts
What’s this formula for:
Inverse square law
  Yes, I love Lucy is crossing the galaxy
  …but it’s a really weak signal
  Reception will be poor

## Slide 19: How far can my wave go?
*In an ideal world
Pr = Power received
d = distance from the source (radius)
Pt = power transmitted
Gt = gain of the antenna
Ae= area covered by the transmitter

## Slide 20
Transmitter
Distance d
Receiver
hb
hm

## Slide 21: Going Further
*Assuming free space
Substitute Ae with receiving antenna gain (Gr) we get:
Stay calm, this isn’t that bad…
= power transmitted (watts)
d = distance in meters
= speed of light

## Slide 22: Propagation
I hope that I have line of sight LoS (or free space)
Reflection
  The radio wave bounces off something larger than the wave
  Like a planet or a building or the atmosphere
Diffraction
  A sharp edge bends the wave
  Edge of a wall
Scattering
  Something smaller than the wave gets in the way
  Like a tree

## Slide 23
Transmitter
d
Receiver
hb
hm
Diffracted Signal
Reflected Signal
Direct Signal
Building
STOP
Scattered

## Slide 24: Signal Processing
Hugely important concept
What’s the shortest/fastest distance between two points?
How many copies of a wave do I receive?
What if the signal reflects?
Flightradar24.com

## Slide 25
Classification Band | Initials | Frequency Range | Characteristics
Extremely low | ELF | < 300 Hz | Ground wave
Infra low | ILF | 300 Hz - 3 kHz | 
Very low | VLF | 3 kHz - 30 kHz | 
Low | LF | 30 kHz - 300 kHz | 
Medium | MF | 300 kHz - 3 MHz | Ground/Sky wave
High | HF | 3 MHz - 30 MHz | Sky wave
Very high | VHF | 30 MHz - 300 MHz | Space wave
Ultra high | UHF | 300 MHz - 3 GHz | 
Super high | SHF | 3 GHz - 30 GHz | 
Extremely high | EHF | 30 GHz - 300 GHz | 
Tremendously high | THF | 300 GHz - 3000 GHz | 

## Slide 26: Waves have properties
Skywaves for example, love to reflect
Different kind of skywave-->

## Slide 27: Ride the Waves
How far can you go?
FM vs AM are great examples
  AM: 535-1705kHz
  FM: 88 – 108 MHz
Basically: AM = big waves
      FM = little waves

## Slide 28: Ionosphere Reflection
AM Radio waves refract from the ionosphere
FM waves blast right through
Where do they go?
  AM: China
  FM: Mars
FM -> height is key, AM -> not really
Ionosphere is really good at refracting at night
AM
  Reduces power, directional antennas, shutdown

## Slide 30: Scales
Small-scale
  Signal variation/fading over a short distance
Large scale
  Signal variation/fading over a long distance
Diffraction & scattering -> small scale
Reflection -> large scale