## Slide 1: Signal Degradation

## Slide 2: Review
Channels
  2 Control Channels
  2 Data Channels
Waves travel at the speed of?
  Based on this we can calculate wavelength
Waves propagate differently
  Large wavelengths create skywaves

## Slide 3: Words have meanings
Isotropic
  Equal in all directions
Are antennas isotropic?

## Slide 4: Antennas
Omnidirectional
  Waves propagate evenly in all directions
  Poor levels directly above/below the plane
  Cell phones, FM Radio, wifi (usually)
  Di-pole
Directional/point to point

## Slide 5: Power Gain (or just gain)
Measurement of antenna’s electrical efficiency
  How well do I transfer electrical signal to waves
  Or vice versa
Ratio of power to theoretical perfection
  Perfection == lossless isotropic antenna
  Usually measured in decibels isotropic (dBi)
  (Can also be dBd, lossless half-wave dipole antenna)
    Dipole antennas are more common
  dBd = dBi – 2.15

## Slide 6: Our radio transmissions degrade
Path Loss Lp
  Reduction in “power density” over wide areas
  Factors- distance, frequency, land
Slow Fading Ls
  Small area problems
  Building, road, etc
Fast Fading LF
  Caused by motion of MS
  Things near transmitter, like raindrops

## Slide 7: Path Loss
Talked briefly before
Urban areas make signal propagation problematic
Thus, better signal in open areas

## Slide 8: Doppler Effect
If you’re moving, your frequency changes
This is called Doppler shift

## Slide 9: Doppler Shift
If you’re a new-age goat with a cellphone, things get messy
fd = Doppler shift
fc = frequency of source carrier
fr = frequency of received signal
v = velocity (m/s)
= carrier wavelength
= Radians
Source carrier wave ->
Source carrier wave ->
Goat ->
*Assume the goat runs fast
Apparently a “goat tower” is a thing ->
*goat towers typically house goats, not cellular transceivers, but I’m no goat expert; I have no proof one way or the other
What frequency does the goat actually receive?
Goat tower broadcasts at 1500 MHz
Assume the goat is really fast: 250 m/s
He’s at an 85 from the carrier wave

## Slide 10: Where is the Doppler effect a big deal?
Walking?
Driving?
Driving really fast?
Flying?

## Slide 12: What about really fast?
http://io9.gizmodo.com/5786083/what-are-the-fastest-spacecrafts-ever-built
http://descanso.jpl.nasa.gov/DPSummary/Descanso4--Voyager_new.pdf

## Slide 13: Spacecraft!
Spacecraft tend to move rather quickly
  Their speeds need to be accounted for in signal processing
Redshift vs blueshift?
  Visible light exhibits the Doppler effect

## Slide 14: ISL
Time
Time
Time
Received signal (short delay)
Received signal (long delay)
1
0
1
Propagation time
Delayed signals