## Slide 1: Error Control

## Slide 2: Where we are…
Starting Chapter 4 in book

## Slide 3: Review
Doppler Effect
ISL
  Refraction
  Reflection
  Scattering
Why do we need signal processing?

## Slide 4: Problems
Situations exist with low transmit power
  Short range devices
  FCC FTW
Things get in the way
  Reflection
  Diffraction
  Scattering
We need all the help we can get

## Slide 5: Channel Coding
Add some data about our data
Cons: We consume more bandwidth
Pros: Reconstruct data
Basically: we can relate redundancy data to original data
  Reconstruct if a piece is missing

## Slide 6: Channel Coding Works Well
Most of the time
Raw datastreams (like an HTML page)
Others, not so well
  Compressed <anything> (audio, video, etc)
  Encrypted stuff

## Slide 7: Error detection vs prevention
Error detection = super easy
In your computer -> super useful
In wireless transmissions -> not particularly useful
  Possibly even useless
  We want to avoid data retransmissions

## Slide 8: Solving Data Loss
Goal: transmit enough extra data (redundant data)
  Allow receiver to recover errors
  Not require sender to re-transmit
Two Categories:
  Cyclic Redundancy Check (CRC)
  Automatic Repeat reQuest (ARQ)
  Forward Error Correction (FEC)

## Slide 9: Easy way first…
Parity bit
Answers the question:
  Is the data I’m supposed to get even or odd?
Even parity example:
  I want to transmit 1100110
  There are 4 bits (4 1’s in the data)
  We’ll attach a 0 to the end and transmit:
  11001100 -> transmitted data
  1100110 -> actual data

## Slide 10: Cyclic Redundancy Check
Used to detect accidental changes to data
  See it in hardware a lot!
Very fast, very easy
Does not solve data loss, only problem detection
  1, 58, 54, 12, 54, 12
  Flatten the data: 15854125412
  Mod 16: 4

## Slide 11: Automatic Repeat reQuest (ARQ)
…Also doesn’t really solve error correction problems…
See in the OSI model layers
  Less likely w/internal hardware
Used in LTE & EVDO networks
  *A variation of it anyway
Stop-and-wait ARQ  wait for an ACK before sending next frame
  Really slow
Go-Back-N ARQ  I number each frame and ACK what I’m currently reading
  May replay good packets
Selective Repeat ARQ  Resend me this one bad frame
  Powerline Ethernet uses this, TCP sort of does as well

## Slide 12: Stop-And-Wait
Transmitting data
1
Time
Received data
1
2
3
Time
ACK
ACK
NAK
Output data
1
2
3
Time
Error
3
3
2
Retransmission
ACK: Acknowledge
NAK: Negative ACK

## Slide 13: Go-Back-N
1
Time
Received data
NAK
Output data
Time
Error
Go-back 3
2
3
4
5
3
4
5
6
7
5
1
Time
2
3
4
5
Error
NAK
Go-back 5
1
2
3
4
5
Transmitting data

## Slide 14: Selective-Repeat
Transmitting data
1
Time
Received data
NAK
Error
Retransmission
2
3
4
5
3
6
7
8
9
7
1
Time
2
4
3
6
8
7
Error
NAK
Retransmission
5
9
Buffer
1
Time
2
4
3
6
8
7
5
9
Output data
1
Time
2
4
3
6
8
7
5
9

## Slide 15: Forward Error Correction (FEC)
Goal: allow the receiver to correct any mishaps on their own
Lots of options here:
  Interleaving is what we’ll talk about

## Slide 16: Some other choices:
AN codes
BCH code
Berger code
Binary Golay code
Constant-weight code
Convolutional code
erasure correcting code
Expander codes
Fountain code
Fountain codes
Gallager code
Golay codes
Goppa code
Group codes
Hadamard code
Hagelbarger code
Hamming code
Latin square based code
Lexicographic code
Long code
Low-density parity-check code
LT code
m of n codes
Online code
Polar code
Raptor code
rateless erasure correcting code
rateless erasure correcting code
rateless erasure correcting code
Reed–Muller code
Reed–Solomon error correction
Repeat-accumulate code
Repetition codes,
sparse graph codes
Spinal code
Tornado code
Triple modular redundancy
Turbo code
Walsh–Hadamard code

## Slide 17: Interleaving -> Forward Error Correction
One FEC method
FEC is important -> what if you’re a TV camera
  Drop a few frames, can you resend them?
Interleaving is important for FEC, used/reused in other methods

## Slide 18
a1, a2, a3, a4, a5, a6, a7, a8, a9, …
Input data
a1, a2, a3, a4 a5, a6, a7, a8 a9, a10, a11, a12 a13, a14, a15, a16
Write
Read
Interleaving
a1, a5, a9, a13, a2, a6, a10, a14, a3, …
Transmitting data
a1, a2, a3, a4 a5, a6, a7, a8 a9, a10, a11, a12 a13, a14, a15, a16
Write
De-Interleaving
a1, a2, a3, a4, a5, a6, a7, a8, a9, …
Output data
a1, a5, a9, a13, a2, a6, a10, a14, a3, …
Received data
Through Air
Read

## Slide 19: Burst Errors
These ones are tough to solve
  Losing one or two bits, no biggie
Burst error -> lost a large chunk of transmitted data
  Usually see the term “symbols”
  For our sake, a symbol is a 1 or a 0

## Slide 20: Example:
Original data: ThisIsAnExampleOfInterleaving…
Received data: ThisIs______pleOfInterleaving…
Conceptually, this is tough to fix

## Slide 21: Enter: interleaving
Original data: ThisIsAnExampleOfInterleaving…
Transmitted Data: TIEpfeaghsxlIrv.iAaenli.snmOten.
Burst Error: TIEpfe______Irv.iAaenli.snmOten.
De-interleaving: T_isI_AnE_amp_eOfInterle_vin_...
The whole purpose: no whole piece of data is ever lost
  Just a couple bits here and there