## Slide 1: Back to Signal

## Slide 2: Review
FDMA
TDMA
CDMA
TDD
FDD

## Slide 3: Space Division Multiple Access
I’m pointing my signal at YOU
  And only you…
Basically, directional antennas on BS and MS
  Can reuse channels
  No interference
  High quality signal
Problems
  Tech is fairly new
  How many antennas can you hang from a tower?

## Slide 4
MS1
MS2
MS3
BS
Beam 1
Beam 2
Beam 3

## Slide 5: Big Advantages of each:
FDMA
  Really easy
TDMA
  Flexible growth
CDMA
  Nearly unlimited growth?
SDMA
  Infinite capacity, pair with CDMA for extra goodness

## Slide 6: Problems
FDMA
  Wastes spectrum, guard bands, no changing frequencies
TDMA
  Needs guard space + time sync issues
CDMA
  Requires signal processing + power levels
SDMA
  Mobile clients are tough to handle

## Slide 7: Where do we use them?
FDMA
  Radio & TV
TDMA
  Mostly GSM, 2G & 3G
CDMA
  2.5 and 3G Communications
OFDM
  The 4G’s
SDMA
  Satellites

## Slide 8: Mobile Infrastructure

## Slide 9: What we’ve covered
What the spectrum is
How spectrum is divided/shared
Protocols used to actually make the sharing work
Basic communication methods of mobile devices
Problems that can exist with wireless communication

## Slide 10: Where we’re going next
Cellular specific stuff
  How the phone infrastructure works
  Devices roaming on wireless networks
  Handling massive data duplication to several devices
Femtocells/microcells
Network protocols used for communication
Infrastructure needed for cellular networks
802.11
Other wireless tech

## Slide 11: MS Mobility
Ideally… a MS can communicate with the world
  From anywhere in the world
  While moving someplace else in the world
Factors that impact this:
  Coverage of cellular networks
  Algorithms for negotiating handoffs
    What protocol do you connect with?
  Routing traffic over wired backbone

## Slide 12: Pieces to the Network
Pieces of cellphone networks
  BS/MS
  Base Station Transceiver System (BTS)
  Authentication Center (AUC)
    Auths people
  Equipment Identity Register (EIR)
    Can be combined with AUC
    Tracks devices
  Base Satiation Controller (BSC)
    Uplink of BTS
  Home Location Register (HLR)
    Where are you from?
  Visitor Location Register (VLR)
    Where are you currently?
  Mobile Switching Center (MSC)
    Controller of multiple BSC
  The gateway
    Link out to the world
      Typically: PSTN or ISDN

## Slide 13
MSC
…
HLR
VLR
EIR
AUC
Gateway MSC
MSC
…
PSTN/ISDN
BSC
BTS
BTS
BTS
MS
Base Station System
BSC
BTS
BTS
BTS
…
MS
Base Station System
…

## Slide 14: Outbound Connections
PTSN
  Public Switched Telephone Network
  Basically: all the telephone circuits in a network
  Analog
  Back from the golden days
  Depreciating
ISDN
  Integrated Services Digital Network
  Digital phone services
  Faster services
  Can operate over IP
  Integrates voice + data
  Many types of ISDN
    US mostly uses PRI (T1, T2, etc)

## Slide 15: PSTN
Public Switched Telephone Network
POTS
Standard phone calls sort of system
Makes use of digital and analog switching
  Can be carried over ethernet
  Most cellular towers now carry signal over ethernet

## Slide 16: Local Exchange Carrier
The final mile in delivering phone service
Most companies called ‘Baby Bells’
  Split up Bell phone company
Handle internal/local calls
  Route long distance calls outside of their network
When calls leave this internal network, we get long distance

## Slide 17: Switching
Connecting two digital or analog circuits for talking
Now digital (in most places)
  Carry data and voice now
Makes decisions if data is local or not
  Uplinks data on a trunk to another carrier
Area codes are used to determine location

## Slide 18: What makes a phone number
Country code
  Usually prefixed with a +
  1 for us & Canada
  44 for UK
Regional numbering plan
  North American Numbering Plan
  Area codes!
  Fixed 3 digital in US & Canada
  Varies between 2-5 in UK, Germany, Austria
Next part is for subscriber
Subscriber can identify carrier
  Not always, but often
Typically, subscriber is broken into
  Few digits for the geographic area/exchange
  Last few digits for the specific person
(605) 256 5849
605 256 5849
+1 605 256 5849
https://en.wikipedia.org/wiki/List_of_North_American_Numbering_Plan_area_codes#United_States

## Slide 19: Special Country Codes
Satellite phone systems
  Use a different country code…. Because geography
Inmarsat: +870
+888 - international disaster relief ops

## Slide 20: Extensions
PBX -> private branch exchange
Run a phone switch within a particular network
Basically: uplinks to Local Exchange handle outbound calls
Calls routed internally don’t touch outside
  Can save tons of money!

## Slide 21: Overall Connections
Last Mile – Carrier to customer
Trunks – link between LEC offices
  Can be T1, T3, ATM, Ethernet
PRI- Connection to an outside voice system

## Slide 22: Trunks Around the World
Fiber optic cabling crosses all over the US
Also under oceans
Super high bandwidth- upwards of 100gb/s
http://www.submarinecablemap.com

## Slide 23: How Connections Are Sold
T1 – 1.5 Mbps
  Phasing out for the most part
T3/DS3 - 45Mbps, but often sold as fractional links
OCn – Optical Carrier (SONET)
  OC1
  OC3
  OC… n = 51.84 Mbps
  OC192
  OC-768, about 40Gbps

## Slide 24: Backhaul Carrier Equipment