## Slide 1: Mobility

## Slide 2: Review
Backhaul carriers bring data across regions
Regional ‘last mile’ providers bring connections to end users
  Sometimes there’s crossover
The phone system is old and constantly changing
ISDN circuits are going away
  In favor of things like OC connections

## Slide 3: Roaming Process
Your device is constantly looking for signals
  Once it finds one it registers it to a kernel table
  If signals get low, a relocation process beings in user space
The new BS finds the HLR for device, authenticates
Then we register in the VLR, authenticate there too
  Two way pointer is established in each registry
How it works: beacons

## Slide 4: Beacons
A BS is always sending out a beacon signal
  Hey, here I am!
When devices begin to connect, they listen for beacons
Notice how connecting to networks tends to take longer away from home?
  Getting off a plane?
  We have to find a beacon, register the device

## Slide 5: Handoff Types
Soft Handoff
  Works great with CDMA!
  We can overlap signals, no issue talking
  Just need to exchange codes
Hard Handoff
  Signals must be cut first
  TDMA and FDMA use this
  Generally a quick process

## Slide 6: Handoff vs Roam
If we hit another MSC, we’re roaming
  Remember MSC’s use circuit technology generally
    As opposed to IP/packet
  Therefore they must trunk if we move from one to another
Generally GSM/CDMA specific
We’ll come back to roaming…

## Slide 7: LTE Has made handoffs intersting
You can’t migrate from VoLTE to: anything else
Migrating from “regular” LTE to CDMA calls?
  No problem, the circuit just redirects
CDMA to LTE?
  Avoid the problem, just keep you on CDMA for now