## Slide 1: Telephone Infrastructure

## Slide 2: Today’s Topics
PSTN
  Connection types
  How calls are routed
  Who handles carrying these signals
What do you shop for when connecting to the world?

## Slide 3: Review
We’ve talked a ton about signal modulation
http://www.engadget.com/2015/09/30/freevolt-free-energy/
Pieces of a cellular network
  HLR/VLR Location Registers
  Base Station Controller
  Authentication and Equipment registration
  Gateway out to the world

## Slide 4: PSTN
Public Switched Telephone Network
POTS
Standard phone calls sort of system
Makes use of digital and analog switching
  Can be carried over ethernet
  Most cellular towers now carry signal over ethernet

## Slide 5: Local Exchange Carrier
The final mile in delivering phone service
Most companies called ‘Baby Bells’
  Split up Bell phone company
Handle internal/local calls
  Route long distance calls outside of their network
When calls leave this internal network, we get long distance

## Slide 6: Switching
Connecting two digital or analog circuits for talking
Now digital (in most places)
  Carry data and voice now
Makes decisions if data is local or not
  Uplinks data on a trunk to another carrier
Area codes are used to determine location

## Slide 7: What makes a phone number
Country code
  Usually prefixed with a +
  1 for us & Canada
  44 for UK
Regional numbering plan
  North American Numbering Plan
  Area codes!
  Fixed 3 digital in US & Canada
  Varies between 2-5 in UK, Germany, Austria
Next part is for subscriber
Subscriber can identify carrier
  Not always, but often
Typically, subscriber is broken into
  Few digits for the geographic area/exchange
  Last few digits for the specific person
(605) 256 5849
605 256 5849
+1 605 256 5849
https://en.wikipedia.org/wiki/List_of_North_American_Numbering_Plan_area_codes#United_States

## Slide 8: Special Country Codes
Satellite phone systems
  Use a different country code…. Because geography
Inmarsat: +870
+888 - international disaster relief ops

## Slide 9: Extensions
PBX -> private branch exchange
Run a phone switch within a particular network
Basically: uplinks to Local Exchange handle outbound calls
Calls routed internally don’t touch outside
  Can save tons of money!

## Slide 10: Overall Connections
Last Mile – Carrier to customer
Trunks – link between LEC offices
  Can be T1, T3, ATM, Ethernet
PRI- Connection to an outside voice system

## Slide 11: Trunks Around the World
Fiber optic cabling crosses all over the US
Also under oceans
Super high bandwidth- upwards of 100gb/s
http://www.submarinecablemap.com

## Slide 12: How Connections Are Sold
T1 – 1.5 Mbps
  Phasing out for the most part
T3/DS3 - 45Mbps, but often sold as fractional links
OCn – Optical Carrier (SONET)
  OC1
  OC3
  OC… n = 51.84 Mbps
  OC192
  OC-768, about 40Gbps

## Slide 13: Backhaul Carrier Equipment