## Slide 1: Mobility

## Slide 2: Review
Backhaul carriers bring data across regions
Regional ‘last mile’ providers bring connections to end users
  Sometimes there’s crossover
The phone system is old and constantly changing
ISDN circuits are going away
  In favor of things like OC connections

## Slide 3: Roaming Process
Your device is constantly looking for signals
  Once it finds one it registers it to a kernel table
  If signals get low, a relocation process beings in user space
The new BS finds the HLR for device, authenticates
Then we register in the VLR, authenticate there too
  Two way pointer is established in each registry
How it works: beacons

## Slide 4: Beacons
A BS is always sending out a beacon signal
  Hey, here I am!
When devices begin to connect, they listen for beacons
Notice how connecting to networks tends to take longer away from home?
  Getting off a plane?
  We have to find a beacon, register the device

## Slide 5: Factors for Handoffs
Either a BS or MS can start a handoff in cellular networks
Factors:
  Number of MS in a cell
  Number of MS moving from a cell
  Number of calls in the cell
  Number of MS moving into the cell
  Number of calls ending in a cell
  Number of calls handed off to others

## Slide 6: Handoff Types
Soft Handoff
  Works great with CDMA!
  We can overlap signals, no issue talking
  Just need to exchange codes
Hard Handoff
  Signals must be cut first
  TDMA and FDMA use this
  Generally a quick process

## Slide 7: Handoff vs Roam
If we hit another MSC, we’re roaming
  Remember MSC’s use circuit technology generally
    As opposed to IP/packet
  Therefore they must trunk if we move from one to another
Generally GSM/CDMA specific
We’ll come back to roaming…

## Slide 8: Device Registration
Two old standards in the US <- used to manage handoffs
  Advanced Mobile Phone System (AMPS)
    True first cellular system
    Used FDMA
    Older analog system finally shutdown
  Cellular Digital Packet Data (CDPD)
    Also phased out
    Used by AT&T a wee bit
    Used by public safety systems

## Slide 9: What we have now
CDMA2000
  Three primary modes
  1X- basically, 1X the bandwidth
    Whopping 153 kb/s
  1xEV-DO
    Hybrid of CDMA and TDMA
    Likely what we think of with 3G
    Can operate up to around 14Mb/s (but no US carrier will install it)
    Usually bursts around 2-3Mb/s though
Expected to be phased out by 2021

## Slide 10: LTE
Next step from GSM and CDMA
Entirely IP based system
See around 20 different bands of frequency around the world
Dynamic channel bandwidth
  Designed to migrate from old technologies
Uses TDD and FDD <-for uplink
Cell size can be between 30 feet and 62 miles
At least 200 active clients/5MHz

## Slide 11: LTE Legacy Bits
CDMA, GSM use circuit switching for voice calls
  Dedicated physical (or digital) path
  Not using packets
LTE wants to be all IP/Packet based, so this is an issue
  VoLTE <- voice over LTE <- Your phone probably/maybe supports this!
    Legit, very clear voice signal, 6-way calling
    Also includes video calling natively
      Verizon bills audio usage against airtime/minutes
        But not for the video stream…
  CSFB <- Circuit switched fallback
    Consolation prize, we adapt circuits for LTE
Notes: Cir

## Slide 12: LTE Has made handoffs intersting
You can’t migrate from VoLTE to: anything else
Migrating from “regular” LTE to CDMA calls?
  No problem, the circuit just redirects
CDMA to LTE?
  Avoid the problem, just keep you on CDMA for now

## Slide 13: HLR and VLR are great
Phone home to ensure where we’re at
But how do I even know you’re legit?

## Slide 14: The Authentication Center (AUC)
Authenticating devices is a big deal
  And everyone does it differently
CDMA vs GSM
  The battle went on…
  GSM sort of Won

## Slide 15: GSM and LTE Authentication
Authentication is based on a SIM card
  Not necessarily the device
This means: we can swap cards and our device *should* move
  This is the case with Spring & AT&T + most of Europe
  Networks mixed with LTE and GSM
Verizon is a bit different…
  It’s a mix of LTE and CDMA

## Slide 16: CDMA Authentication
We white-list CDMA devices for authentication
CDMA Devices have an ESN (but technically now use MEID)
  Electronic Serial Number
Made up from:
  14 bits of manufacturer code
  18 bits of device identifiers (used to be 14)
  24 bits based on a SHA1 hash of MEID
    MEID literally is a MAC address counterpart
    Region code, manufacturer code, and serial number in hex
Now we technically use “pESN” psuedo ESN

## Slide 17: ESN -> you’ll never find it
Since the pESN is a function of the MEID
  (We ran out of ESN’s long ago)
CDMA networks store a random key (that the AcU & device know)
  The key can rotate if needed (called an a-key)
BS sends phone & AcU a random number (MSC -> VLR -> HLR -> AuC)
  Phone uses number (a-key) ESN + random number to calculate a value
  So does the AuC
Results of calculation sent to BS
  BS compares what device and AuC came up with
A similar process is used to create an encryption key

## Slide 18: GSM -> SIM Card
We white-list SIM cards for authentication
SIM cards have a Ki key burned in at manufacture
  Value is also registered with the AuC
We then use the IMSI (identifies the carrier)
  With the Ki to create a challenge/response key Kc
In essence-> the device authenticates the network
  If the authentication is successful, we move on
This is why GSM devices aren’t carrier specific, but SIM cards are
  This is also why GSM devices were [are] susceptible to MitM attacks

## Slide 19: Random Value Recap
IMEI -> International Mobile Station Equipment Identity
  Hardware identifier of GSM and LTE devices (not SIM cards)
ICCID -> Integrated Circuit Card Identifier
  Hardware serial number of a SIM card
MEID -> Mobile Equipment Identifier
  Used to identify a CDMA device
IMSI -> International Mobile Subscriber Identity
  Value that identifies a GSM or LTE carrier