## Slide 1: Wireless Signals

## Slide 2: Review
CDMA2000 vs GSM
  Changed a lot over the years
LTE
  IP telephony vs legacy PTSN
How do devices identify themselves
How is LTE different
  Frequency bands

## Slide 3: Cell Signal
Obviously a huge issue
Geographic vs urban… etc
Issue: traffic origionation
  50% of voice calls
  70-80% of data transactions
  They start indoors

## Slide 4: Problem: waves vs walls
Higher frequency wavelengths
  Properties of them
  Great at straight lines
  Good at atmosphere
  Not so good with walls
Proof of concept:
  GPS vs FM
    One is much easier to receive indoors

## Slide 5: Cell Sizes
Standard <- 35km
Microcell <- 2km
  Urban Areas
  Mall or stadium
Picocell <- 200 meters
  Office buildings
Femtocell <-10 meters
  House

## Slide 6: Femtocells
9.6 million femotcells deployed world-wide
  Account for 56% of base stations
Obvious perks
  Better signal quality
  Better signal strength
    Battery life!

## Slide 7: Femtocells- Carrier Perks
Happy customers
Ease load on macro/other cells in the area
  Can save huge amounts of money
Use spectrum more efficiently

## Slide 8: Femtocells- The downsides
Interference
  Carrier can’t really control distances between cells
  Femtocell may interfere with other macrocells too
QoS
  QoS is huge for all internet traffic
  Provides traffic prioritization
    DSU Examples
  HUGE in the VoIP area (nearly required)
  QoS typically doesn’t exist in consumer networks

## Slide 9: Femtocells- The downsides
Access control
  Open access mode (open subscribers group OSG)
  Closed assess mode (closed subscribers group CSG)
  Hybrid -> a little of both
    Common in the US with E911
Handoffs
  Negotiating handoffs isn’t really a thing
Sync <- time!
Securing the device
  Sniffing traffic from the endpoints

## Slide 10: Femtocell Components
Femtocell itself
  Has a wireless radio
  Wired network for uplink
Femtocell Gateway
  Operated by the wireless carrier
  All femtocells forward all traffic
  Converts IP traffic/phone circuits
Macrocells
  Handle tracking of F-BS
  Handoffs to each

## Slide 11: Signal Strength
Major factor in determining your associated BS
Usually MS and BS negotiate this
Signal Strength
  RSRP <- LTE Signal strength, >-90dBm to -120dBm
  RSSI <- Received Signal Strength Indicator (non-LTE) (>-70 to -100dBm)
  Qrxlevmin <- what’s the minimum RSRP value I’ll take?
Signal Quality
  ECIO -> Energy to Interference Ratio
  RSRQ- Reference Signal Received Quality
  SINR – Signal to Interference plus Noise Ratio
Where are the cell towers at?
  http://www.antennasearch.com

## Slide 12
Signal Strength
  RSRP <- LTE Signal strength
  RSSI <- Received Signal Strength Indicator
Signal Quality
  ECIO -> Energy to Interference Ratio
  RSRQ- Reference Signal Received Quality
  SINR – Signal to Interference plus Noise Ratio