## Slide 1: WiFi

## Slide 2: Review
802.11
  Section of IEEE standards document
  Uses ISM bands (industrial scientific medical)
  Common: B, A, G, N, AC
Adaptive Rate Selection
  What does it do?
  Why?

## Slide 3: 802.11 ABC’s
A, B, and G
  Very closely related
  B -> baseline technology
  A -> frequency + new tech
  G -> hybrid
N, AC
  New age tech

## Slide 4: Channel Diagram

## Slide 5: Wireless Spectrum
9-100 Khz- Aircraft, ship navigation
100Khz-1Mhz: AM Radio
Around 10 Mhz: Shortwave Radio
Around 100 Mhz: FM Radio
Between FM and 1Ghz: TV
1Ghz: Cell Phones
10 Ghz + WiMax and Satellite

## Slide 6: WiFi Components
Hardware makes a difference
Chipset
Vendor
Antenna

## Slide 7: Chipset
Tons of options
  Generally -> strength vs power use
Most physical network adapters
  Realtek and Intel
Intel makes a lot of chips <- this makes sense
Ralink makes them too
Power/signal/other factors
  Features!

## Slide 8: 802.11 Adapter Modes
Requires hardware and OS support
Various potential modes
  Access Point (ExtAP)
  Station (ExtSTA)
  Network Monitor (NetMon)
  Ad Hoc

## Slide 9: Alfa AWUS051NH
Chipset supports monitor mode
  This is helpful…
    ...for sketchy stuff
Kali already has drivers
Please don’t use 64 bit Kali…

## Slide 10: Watch wireless connect
Open Wireshark
Applications>Internet>Wireshark
Select wlan0, click Start

## Slide 11: And…. Nothing Happens…

## Slide 12: Connect to a Network
Network Manager >
  Select your network

## Slide 13: airmon-ng
Enables monitoring of wireless interfaces
Forces your adapter into “monitor” mode
  Basically: creeper mode

## Slide 14: airmon-ng
airmon-ng <- will list adapters
  Also tells you if NetMon is supported
airmon-ng start wlan#
  Puts specified adapter into monitor mode
  Creates new ‘interface’ in interface list
airmon-ng check kill
  Kill off all PID’s that are associated with the adapter
Notes: Running airmon-ng by itself will list all of the current wifi adapters and tell you if any monitors exist
Airmon-ng check kill will find all of the programs that are using the wireless adapter and kill them off

## Slide 15: Interesting Stuff
Channel can be important
Adapter can only listen to 1 channel at a time
Getting stuck on a channel can be a problem
Moving channel to channel can be a problem
*It’s not supposed to be a problem

## Slide 16: Watch wireless connect
Open Wireshark
Applications>Internet>Wireshark
Select mon0, click Start

## Slide 17: Problem
Your Routers/APs spill all of their details...
  Broadcast TONS of info that we LOVE to have!
  BSSID: Basic service set identification
    Contains: SSID and MAC Address
      SSID: Service Set Identifier
      MAC: Your hardware address
  What if we hide this info??