## Slide 1: Terrible Ways of Securing Wifi

## Slide 2: Review
Stuff and things

## Slide 3: Problem
In a single AP environment, wireless is easy
Multiple APs, problems ensue:
  User connects to a network
  Network consists of multiple radios
  Endpoints: can only connect to 1 radio
  How do you pick?
    How do you know it’s the right network?
    Roam from radio to radio?

## Slide 4: Terms!
SSID
  Service Set Identifiers
  Broadcast name of the network
BSSID
  Basic Service Set Identifier
  MAC address of a radio
  MAC address of a radio/SSID combo
ESSID
  More or less same as SSID

## Slide 5: Basic WiFi Tools
iwconfig
  Sort of ifconfig for wifi
iwlist interface scan
  Show me what you got!
iwevent
  Monitor events on the adapter

## Slide 6: Problem
Your Routers/APs spill all of their details...
  Broadcast TONS of info that we LOVE to have!
  BSSID: Basic service set identification
    Contains: SSID and MAC Address
      SSID: Service Set Identifier
      MAC: Your hardware address
  What if we hide this info??

## Slide 7: Hiding Info
Just like on Facebook
  You can *hide* info
  …but you’re really only hiding it from yourself
SSID’s are the same way
We can legitemetly hide an SSID
  AP will refuse to broadcast it
BUT: in order to connect, you have to SHOUT it outloud
Encrypted or not, you have to say the secret
  Just like BSSID <- can’t be hidden

## Slide 8: Hiding an SSID
Easy to do
We just need to wait for someone to connect
  They’ll have to rebroadcast the SSID
    (the client has to, not the AP)
Start airmon
  airmon-ng start wlan#
Start airodump w/monitor interface
  airodump-ng mon#

## Slide 9: airodump-ng
What does this do?
Another piece of the Aircrack-ng package
Captures raw 802.11 frames
Does all sorts of fun stuff with them!
  Pairs with GPS
  WEP initialization vectors
  Lists networks as it sees them
Can also intake pcap data

## Slide 10: Airodump fields
BSSID
  MAC of the AP
PWR
  Signal level seen by the chipset
RXQ
  Received Quality
  Factor of packets successful over last 10 seconds
Beacons
  Announcemnt packets from AP
  About 10/second @ low bitrate
# Data
  Number of captured data packets
#/s
  Packets per second
CH
  Channel
MB
  Max speed advertised
ENC
  Encryption algorithm

## Slide 11: airodump
Airodump has many flags
--bssid is a big one
  Aka: please only listen to this one
Hugely important when archiving
  Or being in a place with lots of APs

## Slide 12: MAC Filters are lame
Use airodump, find a connected client
  Can’t hide MAC addresses
  Must be sent in clear
Spoof your MAC address
  Profit

## Slide 13: Spoof a MAC?
Shut down the interface
  ifconfig wlan# down
Specify the MAC
  ifconfig wlan# hw ether MAC_ADDY
Profit/Connect/Win/?