## Slide 1: Terrible Ways of Securing Wifi

## Slide 2: Review!
ESSID
BSSID
Hiding an SSID
  Why doesn’t it work?

## Slide 3: 802.11 Frame
Data frames -> pretty self explanatory
Association Request Frame-> Asks AP to sync time and ready resources for client
  Contains NIC info, and SSID
Beacon frame-> sent out by the AP advertising
  Contains timestamp, SSID, hardware
Probe Request -> Frame from client asking about AP’s in the area
Probe response frame -> answer to request questions, similar to a beacon

## Slide 4: Wireshark Frame Types
Association Request- wlan.fc.type_subtype==0
Assoc Response- wlan.fc.type_subtype==1
Probe Request- wlan.fc.type_subtype==5
Beacon wlan.fc.type_subtype==8

## Slide 5: MAC address filters
Another stupid security mechanism
Somewhat effective with wired networks
  Spoofing still somewhat possible
  Discovery is harder
In wireless, MAC filters are stupid
  You ANNOUNCE your MAC address
  Anyone can spoof it
  Doesn’t prevent any sort of eavesdropping

## Slide 6: MAC Filters are lame
Use airodump, find a connected client
  Can’t hide MAC addresses
  Must be sent in clear
Spoof your MAC address
  Profit

## Slide 7: Spoof a MAC?
Shut down the interface
  ifconfig wlan# down
Specify the MAC
  ifconfig wlan# hw ether MAC_ADDY
  ifconfig wlan# up
Profit/Connect/Win/?

## Slide 8: Presentation
How are things going?