## Slide 1: Other Wireless Goodies

## Slide 2: Technologies We Use
Zigbee
Xbee

## Slide 3: Zigbee
IEEE 802.15.4 tech
Personal Area Network (WPAN)
Focused on low power / low range
  vs WiFi or Bluetooth
300 feet absolute max distance
  Usually around 20-30 feet
Mesh network
  Can extend range from device to devie

## Slide 4: Zigbee Characteristics
Very low latency
Also low bandwidth -> 250kb/s
Uses ISM bands
  2.4 GHz
  Also uses 915MHz
Great for battery based devices

## Slide 5: Where Zigbee is used
Home automation stuff
  Lights, temperature, motion sensors
Smoke detectors
Door locks
Basically:
  Any place where wires are hard and lots of data isn’t needed
Medical data
Industrial controls
Smart meters

## Slide 6: Tech Specs
16 possible channels @ 2.4 GHz
  5 MHz spacing between
Three key devices
  ZigBee Coordinator <- Root device in the network
    Only one device possible ni the protocol
    Knows the trust / crypto information
  ZigBee Router <- Can route Zigbee frames over IP networks
  ZigBee Device <- Really dumb device, knows just enough to talk to controller

## Slide 7: Device Properties
Some devices can be continually receiving
  Beacon vs non-beacon mode
Zigbee devices are typically either passive or highly active
Examples:
  Light switch -> only needs to send signal when changed
  Light bulb -> always powered, always receiving, always active
Beacon enabled networks
  Devices sleep and periodically wake up

## Slide 8: Secure Communications
Once network is online…
  Communications are great!
  128-bit AES encryption!
One method of key exchange
  Static entry
  Sadly: this isn’t consumer friendly
We want it automagic! Users can’t be bothered with security
  When joining a new device, we send the network key in the clear

## Slide 9: DIY Short Range Wireless?
Zigbee can be complicated
  Mesh networking doesn’t come easy
  Fairly short range too
  Mostly used in commerical applications
Enter: XBee!
  Very similar technology as Zigbee
  Can be cross compatible in some ways
Inexpensive, can do mesh, easy to access

## Slide 10: XBee: easy for DIY
Zigbee can require licensing with Zigbee alliance
XBee: modules are easy to get
  Even have some + use them
Frequency use
  ISM again, 2.4 GHz, 900 MHz, 860MHz
XBee also makes 802.11 devices
All are fairly cheap to purchase / easy to use

## Slide 11: XBee Details
About the size of a quarter
  Same form factor for all devices
  Neat: interchange radio hardware
  Grab a USB connector for PC
Can be surface mount or external antennas
Pushing for open/public projects:
http://gallery.digi.com