## Slide 1: Today: Planes Are Cool
Seriously: Tons of metal, in the air, really fast.

## Slide 2: ADSB Transmission ->Basics
Planes running into each other is problematic
  Some might say “terminal”
They need to communicate with each other
  Relying on a 3rd party is inefficient
  Unneeded dependencies
Signal is sent in the clear
  Makes working with transmissions easier
  But they’re in the clear
  More on this later

## Slide 3: Fear of electronics
It’ll be a generational thing
  But you all may have experienced it
Electronics + plane = DOOM
Somewhat well founded
  Not by evidence though
Electronics put of EMI
Does it truly interfere?

## Slide 4: Automatic Dependent Surveillance Broadcast
Where it exists:
  Mandatory is most of Australia
  US Requires it in certain aircraft by 2020
    Most commercial aircraft use it now
  Mandatory in Europe for most commercial in 2017
  Canada: pretty much all-in already
    Why is that?

## Slide 5: Tech Specs
Broadcast every second
  Position, Altitude, Velocity, identification
Two styles: ADS-B Out and ADS-B In <- they do the obvious
Frequencies
  1090 MHz -> Aircraft that can operate above 18,000 feet
  978 MHz -> aircraft below 18,000 feet

## Slide 6: Problems
Unauthenticated, good and bad!
  Anyone can receive
  Anyone with a capable radio can transmit
Mystery plans popping up out of nowhere?
Costs -> gotta put these in planes!
  Surprisingly cheap -> around $10K for ADSB-Out only
  ADSB-In / ADSB-Out -> 10-30K

## Slide 7: Totally Different Aircraft Stuff
Malaysia Airlines Flight 370
  Disappeared in the Indian Ocean
  ADSB-Out transmissions turned off
  Too far for radar
Remember when we talked about Inmarsat?
  Satellite communications with the aircraft
  Uploading some sort of data
    Internet, phone calls, whatever, doesn’t matter
  Key thing: communications continued to happen
Problem with MH370: where did it go???

## Slide 8: Direction is important
Factors we know:
  Fuel on the plane
  Were we last saw the plane for sure
  Satellite talked with plane
    Only had certain range
Planes have long range
So do satellites
Limit to that area
  Lots of ocean

## Slide 9: Next steps-> plot a course
We know timestamps of satellite communications
Timestamps
  Plus
Aircraft Range
  Plus
Satellite Range
  Equals
Rings!

## Slide 10: That’s still a lot of ocean

## Slide 11: What if we knew direction?

## Slide 12: Wireless Communications: How can we determine direction or speed?

## Slide 13: Doppler Effect!

## Slide 14: What can be determined
If wavelengths increase vs decrease
  Direction can be determined!
Amount of variation
  Speed can be estimated
Problem
  Still didn’t find plane

## Slide 15: Let’s listen to ADSB!