## Slide 1: OpenBTS Setup

## Slide 2: Tasks At Hand
Get a phone
  If you have a GSM capable phone, you can use it
Install SIM card
  What’s our limitation again?
  Hint: something OpenBTS supports but GSM technically doesn’t
Phones working & not connected to a network
  What calls can they place?

## Slide 3: Assuming radio is all-good…

## Slide 4: OpenBTS
We’re not going to worry about other services for now
Make sure OpenBTS is running (sudo service openbts start)
Open the OpenBTS interface
  sudo /OpenBTS/OpenBTSCLI
Uses key based config
  Want to change GSM.Radio.Attribute to be a 3?
    Type:
    config GSM.Radio.Attribute 3

## Slide 5: Radio Config (GSM.Radio)
Choose our band
  GSM.Radio.Band
  Let’s go for non-US bands (900 mHz)
ARFCN?
  GSM.Radio.C0
  Pick different ones from neighbors
Gain on the radio- tweaking signals
  GSM.Radio.RxGain 10

## Slide 6: Identity Parameters (GSM.Identity)
What are these?
  MCC
  MNC
  ShortName
  LAC, CI, NCC, BCC

## Slide 7: Registration Parameters (Control.LUR)
OpenRegistration- probably disabled
  Set as a regex of IMSIs
  .* -Allow everyone
Message –What do we send as a welcome SMS

## Slide 8: sipauthserve
We need to register subscribers
  Give them a MSISDN
  What’s that??? ^^^
Node manager!
  It’s in /home/openbts/git-openbts/NodeManager
  nmcli.py
Parameters:
  nmcli.py sipauthserve subscribers create <name> <imsi> <msisdn>
  Can also include a Ki as a final parameter

## Slide 9: OpenBTS Nubers!
Calling:
  2600 -> latency test, echo back
  2602 -> test tone
Others:
  411 -> SMS testing
    Replies with Queue length, Load, Your IMSI, MSISDN, Date/Time
  sendsms command

## Slide 10: chans
SNR
  We want this low, signal to noise ratio
TxPwr
  How much power is the handset pushing out?

## Slide 11: Taps!
Control.GSMTAP.GSM
        TargetIP