## Slide 1: Intro to Not-Cellular Stuff

## Slide 2: 802.11
Started in 1997
  802.11-1997 first ever wireless standard
  No one used it
IEEE standard
  Manage/maintain the “Wi-Fi” regulations
Use ISM Bands -> what does this mean?

## Slide 3: 802.11 B
First one commonly seen
Rarely seen now
  Anyone have a device that uses this?
Just under 500’ range
  Typical conditions, line of sight
Lives at 2.4 GHz
  22 MHz channel bands
  13 [14] overlapping channels
  Only 1-11 in USA
Up to 11 mb/s
  Overhead maxes out at about 5 mb/s
Why?
  CSMA/CA
Very susceptible to interference
  Loves ARS
Direct-sequence spread spectrum modulation
  Basically like CDMA

## Slide 4: 802.11 B Channels
Center Frequency Diff Width Overlaps
1 2.412 GHz 5 MHz 2.401–2.423 GHz 2-5
2 2.417 GHz 5 MHz 2.406–2.428 GHz 1,3-6
3 2.422 GHz 5 MHz 2.411–2.433 GHz 1-2,4-7
4 2.427 GHz 5 MHz 2.416–2.438 GHz 1-3,5-8
5 2.432 GHz 5 MHz 2.421–2.443 GHz 1-4,6-9
6 2.437 GHz 5 MHz 2.426–2.448 GHz 2-5,7-10
7 2.442 GHz 5 MHz 2.431–2.453 GHz 3-6,8-11
8 2.447 GHz 5 MHz 2.436–2.458 GHz 4-7,9-12
9 2.452 GHz 5 MHz 2.441–2.463 GHz 5-8,10-13
10 2.457 GHz 5 MHz 2.446–2.468 GHz 6-9,11-13
11 2.462 GHz 5 MHz 2.451–2.473 GHz 7-10,12-13
12 2.467 GHz 5 MHz 2.456–2.478 GHz 8-11,13-14 <-Everyone but USA
13 2.472 GHz 5 MHz 2.461–2.483 GHz 9-12, 14 <-Everyone but USA
14 2.484 GHz 12 MHz 2.473–2.495 GHz 12-13 <- Japan Only

## Slide 5: Channel Diagram

## Slide 6: 802.11 A
Came out the same time as B
Equipment was more expensive/unavailable
Uses 5 or 3.7 GHz <- equipment issues here
  3.7 GHz requires a license
OFDM-only
  No Direct-sequence spread spectrum modulation
Generally 12 channels
  World regulations vary a lot with this

## Slide 7: What makes 802.11 A different?
Higher frequency, less wall penetration
  OFDM helps make up for this a bit
  Also smaller antennas (smaller wavelength)
  Line of sight, only about 400’
Lots of frequencies
  Pick a channel, divide by 64
  These are sub-carriers for OFDM
  Save 12 for guard bands

## Slide 8: Cool 802.11a stuff
Technically, 802.11y**
3.7 GHz band
  3650-3700 MHz technically
Licensed 802.11a bands
  Must pay FCC $$
Transmissions are different
  WAY higher powered transmissions
    Up to 20 watts
    Not to be used indoors!
Roughly 3 mile range

## Slide 9: 802.11g
The good stuff arrives
Big focus: compatibility with 802.11b
  So many devices adopted it
In essence: adopted everything of 802.11a
  Only on the 2.4GHz spectrum
  Big pice: OFDM
When a B device is present, reverts to B speeds
Same channels as B
  Same range too, about 500’

## Slide 10: 802.11n
We love 802.11n!
  Best of both worlds
  Compatibility blending with a/b/g
  Operates on 2.4 and/or 5 GHz
Way faster, up to 600mb/s
MIMO technology
  Multiple input/multiple output
  Requires multiple antennas
  Multiple transcievers
20 or 40 MHz bands
  40MHz, more data
  Can use 2.4, if not interfering
72mb/s
  1 antenna @ 20MHz
  Cheap access points
150mb/s
  2 antennas @ 20MHz
288mb/s
  4X20MHz
600mb/s
  4 antennas @ 40MHz

## Slide 11: 802.11n Strategy
Use 5GHz
  Way more channels typically available
  Less interference
  Go 802.11n clients only
Backwards compatible
  Dual-radio AP’s
  2.4GHz for old clients
  5GHz only for new clients on n
    Catch-> not all n clients have a 5GHz radio

## Slide 12: Herding Sheep
Many clients support 2.4 and 5GHz
  These [newer] clients pick which frequency for n
  Sometimes they pick wrong
  This sucks
Band steering
  Ignore 2.4GHz n requests
  Force them over
40MHz @ 2.4 GHz? Big challenge

## Slide 13: Adaptive Rate Selection
We use a shared medium
  Aka, the air
If I need to re-transmit, it takes up more time
Therefore… if we’re having troubles...
  We have to slow down
High interference/too many users/corrupt data
  Yields ARS
  We slow down the rate of transmission
  Eases re-retransmission rates

## Slide 14: Side Lobes
A pattern of radiation from an antenna is called a lobe
  Main beam has the greatest signal