## Slide 1: Cells!

## Slide 2: Review
Signals degrade, data becomes corrupt
  ISL
  Burst Errors
Enter: signal processing
Methods of getting good data
  Hashing/parity bit/checksums
  Automatic retransmission requests
  Block codes + interleaving

## Slide 3: Cells
Size does matter
Factors
  Number of users
  What are they doing
    Calls vs selfies
  Shape of geography

## Slide 4: Cellular Area
Shape of the cell
  Talked about this before
  Ideally a circle
  Doesn’t fit well in our grids
Pesky planet causes problems again
Area vs channels
  More area : less channels/user
  Less area : more channels / user
  Works well in urban areas
Cell
R
Ideal cell
Actual cell
R
R
R
R
Consolation Prizes

## Slide 5: Reduce the size (if needed)
Urban area, add more cells
Fewer users per cell, smaller cells
Life is pretty good
Downside: handoffs
  People won’t stop moving
  Neither will goats

## Slide 6: Signal Strength vs Handoffs
We know some obvious things
  (to a not so obvious detail)
  Distance <> signal strength
If we control both BS…
  We can play nice
  Allow overlapping signals
Select cell i on left of boundary
Select cell j on right of boundary
Cell j
-60
-70
-80
-90
-100
Cell i
-60
-70
-80
-90
-100

## Slide 7: Life isn’t fair
Or rather, signal strength isn’t
-100
-90
-80
-70
-60
-60
-70
-80
-90
-100
Cell i
Cell j

## Slide 8: The Handoff
Where do we do the handoff?
As we get farther from one BS…
  We’re ideally getting closer to another
Hopefully signal strength is equal within a region
We can define where to handoff from one BS to another

## Slide 9
BSi
Signal strength due to BSj
E
X1
Signal strength due to BSi
BSj
X3
X4
X2
X5
Xth
MS
Pmin
Pi(x)
Pj(x)
BSj
X4
X2
Xth
X4
X2
Xth

## Slide 10: Handoffs Tech
Some tech is better than others at doing a handoff
Generally: Horizontal Handoff
  Roam from one BS to another
Tech that’s good at horizontal handoff:
  Cellular
Not so good:
  Wifi <- IEEE 802.11
Vertical Handoff
  Roam from WiFi to LTE

## Slide 11: Handoff problems
Most of our digital communications are based on what kind of technology?

## Slide 12: Lots of IPs
Paint the scenario:
  You walk from East Hall to Kennedy Center
  You successfully transition (horizontally)
  Move from EH306 throughout EH APs
  Eventually handoff to Kennedy Center
Does your IP address change?
  Does your network change?
What is changing?

## Slide 13: Another Scenario
Let’s say wireless isn’t one flat network
You leave EH and seamlessly roam (horizontally)
  The SSID is still GoTrojans
  Your connection never drops
But… KC is on a separate network
What problem now exists?

## Slide 14: Possible solutions
You kept your IP but moved networks
  These aren’t the IP’s you’re looking for
Two primary options:
  Force you to drop your connection
    This is pretty easy
    (killing wifi, turns out, not that hard)
  Tunnel your IP back home
    New network sees your new IP
    Forms a tunnel back to where it belongs
    Very complicated solution to keep Netflix streaming…
This will come back to play more

## Slide 15: Horizontal was hard…
Vertical is… nearly non-existent
We don’t have a good way to transition you to new tech
Streaming video, lose wifi, video will probably stop
Solutions:
  Handle this in software
Problems:
  Cell carriers want a BS in my house

## Slide 16: Next Problem
Assuming we can handle handing connections from one BS to another…
The spectrum is not wide and vast
  It is, we just don’t have a license to use it
So: frequency reuse
  We have to reuse frequencies (or large chunks of channels)
  But we can’t have 2 BS’s next to each other w/same channels
The answer: SPACE

## Slide 17: Frequency Reuse
We can reuse frequencies in a cell
  Need to space them out
  Physically
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F1
F1
F1

## Slide 18: How far between re-useage?
Reuse factor!
D=distance
N= number of cells/cluster
R=radius of each cell
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F1
F1
F1

## Slide 19: How far between re-usage?
7 cells in a cluster
1km
D=distance
About 4.5km
We can reuse a frequency every 4.5km
  (in this example)
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F1
F1
F1