## Slide 1: Multi-Access

## Slide 2: Review
Size matters
Major battle exists
  Signal strength vs Interference
Co-channel interference vs near channel interference
Sectoring allows for more efficient use
  Dynamic load balancing

## Slide 3: Control Channels
We know we need them
  Manages our communication circuits
Statically allocate or share?

## Slide 4: Multiple Access
Static assignment won’t work
Users are irritating
  Need control channels randomly
  Need for random periods
Makes a control channel an expensive commodity
Central authorization is one good solution
  Kind of like DHCP
  Doesn’t work though- BS needs to initiate channel requests

## Slide 5: Need Sharing
We don’t know who is going to initiate control conversations
  BS or MS
  Different from DHCP -> always client initiated
Ad-Hoc networking
  We all connect to each other
  Need to communicate nicely
One reason why bluetooth doesn’t scale
  (conceptually)
  Can’t handle multiple conversations at once

## Slide 6: Life is like a hub
We all want to talk
Hub’s don’t care
Collisions
  Co channel interference!
We all need to communicate
  We can’t talk at the same time
Send/receive a packet at the same time: collision
Same thing happens in spectrum over the air

## Slide 7: Protocols
The rules we live by!
We need to determine:
  Who is allowed to talk
  How long can they talk for?
  How long does it take to listen?
Two Types
  Contention Based
  Conflict Free

## Slide 8: Channel Sharing Techniques
Static Channelization
  Channel is assigned, never changes over time
Dynamic Medium Access Control
  Channel assignments will change
    We either schedule the change
    Or randomly choose

## Slide 9: Two Styles
Contention Based
  Let’s just talk and hope for the best
  If we interrupt each other…
    The protocol will define what to do
Conflict Free
  We’ll talk so we never interrupt each other

## Slide 10: Contention Based
I’m going to talk
I hope no one else is talking
Two Categories based on how we handle collisions
  Random Access
    We collide, everyone waits a random period of time
    Then retransmit
  Collision Resolution
    Extra Rules define when we transmit

## Slide 11: ALOHA
Created in the 1970’s @ University of Hawaii
You transmit a packet when you want
  Each packet must be the same size
  Recipient has to acknowledge the receipt
  No acknowledgement? Wait a random time and send again
Easy to implement, doesn’t scale well
  After too many users, throughput goes way down

## Slide 12: Slotted ALOHA
Similar story, but we sync up first
Once our clocks are synced, we define slots
Each packet must be the same size
Still can transmit when you want, but must be during a slot

## Slide 13
1
2
Retransmission
Retransmission
3
Slot
Node 1 Packet
Collision
3
No transmission
Nodes 2 & 3 Packets
Time

## Slide 14
Slotted Aloha
Aloha
0.368
0.184
G (=gT)
Throughput S
8
6
4
2
0
0.5
0.4
0.3
0.2
0.1
0

## Slide 15: ALOHA Doesn’t Scale Well…

## Slide 16: CSMA- Carrier Sense Multiple Access

## Slide 17: CSMA
Tons of varieties of CSMA…
But the overall purpose:
Look before you leap
When a timeslot is upon us…
  Quick listen first
  If no one is talking, transmit

## Slide 18: CSMA’s
Nonpersistent CSMA
  Basically just like ALOHA (or slotted) but listens first
1-Persistent CSMA
  Listens, if no one is talking, assume no-one will talk
  Always transmit as soon as it’s quiet
P-Persistent CSMA
  Slotted
  Slots vary in size
  We gamble the likelihood of colliding
    Based on the number of terminals
  Estimate: when should I transmit

## Slide 19
0 1 2 3 4 5 6 7 8 9
Traffic Load G
1.0
0.9
0.8
0.7
0.6
0.5
0.4
0.3
0.2
0.1
0
Throughput S
Aloha
Slotted Aloha
p=1: persistent CSMA
No wait
p=0.5: persistent CSMA
p=0.1: persistent CSMA
p=0.01: persistent CSMA
p=0: Nonpersistent CSMA
Always wait for T units

## Slide 20: More CSMA
The previous CSMA methods have faults
  Even if they’re talking at the same time, they keep talking
CSMA/CD
  Collision detection
  We interrupted each other, let’s stop talking
Ethernet!

## Slide 21: CSMA/CA
Collision Avoidance
Used by 802.11
Everyone listens for traffic
When ready, we listen one more time, then offset a bit
If we have a collision, we increase our offset