## Slide 1: Multi Division

## Slide 2: Review
Multiple control channels are needed
Sadly, not enough for everyone
  We have to share
  Sharing sucks
  A lot
Techniques created to allow sharing
  ALOHA <-- great first attempt, scales poorly. Why?
  Slotted ALOHA. <-- sync time slots
  CSMA <-- a worldly new idea, listen first!
  CSMA/CD <-- great for duplex
  CSMA/CA <-- dynamically predict/avoid collisions

## Slide 3: Being Chatty
Multi radio access methods are important
  Primarily used for control channels
  Data channels are too intensive to share in these ways
The good news
  We can predict a data channel's need!
  Well, not really….
  The control channel will ask for it first

## Slide 4: Brining it all back
ALOHA and CSMA
  Still essential
  Their role: unscheduled and unpredictable transmissions
  Aka: control channels
The MS will ask for the data channel via control
  Control channel will gladly provision access for data

## Slide 5: Multi Division Requirements
Who are you talking to?
  I hear a lot of discussions
  Are any of them meant for me?
  Same issues for BS and MS
An MS needs to keep their BS straight
  There many BS like mine, but this one is mine
  (Not to be confused with the other BSers out there

## Slide 6: Any guesses what protocols we use for data?

## Slide 7: They're back!!
FDMA
TDMA
CDMA
OFDM

## Slide 8: These are divided up
Two core categories
Duplex traffic needs to happen somehow
Frequency division duplex get (FDD)
  Carve out the frequency being used
Time division duplexing (TDD)
  Carve shares out based on time

## Slide 9: So where do they fall?
Our multi access methods can be categorized as:
FDMA
  Clearly a FDD
TDMA
  Mostly TDD
  But has a dash of FDD
CDMA
  Both

## Slide 10: FDMA
FDMA never overlaps a frequency
  Easy to ensure zero interference
Use a frequency synthesizer
  Handles the broadcast on correct channels
Channel Spacing
  Generally:
  Uplinks are separate from down links
  All of the uplink channels are in one block of spectrum
  Individual up/down pairs are separated
Uplink and down link groups are separated by a buffer
  Protecting bandwidth

## Slide 11: FDMA
…
f1’
f2’
fn’
…
f1
f2
fn
Reverse channels
Forward channels
Guard Band Wg
1
2
3
…
N
Frequency
Total Bandwidth W = NWc
4
Sub Band Wc

## Slide 12: TDMA
Same concept as FDMA
  Except…
Now we assign time slots
Sort of like slotted ALOHA
Some differences though:
  Can be FDD or TDD
  Technically becomes FDMA/FDD vs FDMA/FDD
  The division is for up/down links

## Slide 13: TDMA Guard
Now we use time instead of spectrum
…
Time
Frequency
1
2
2
n
…
…
1
2
n
Frame
Frame
Frame
Head
Data
Guard time
n
1

## Slide 14: TDMA Problems
Wide band TDMA can have super high speeds
  But it sucks
TDMA can't handle multi path fading
  Waves bounce around stuff
  Might get delayed between BS and MS
  Terrible deal when the whole protocol is based on time
Lots of control channel time spent on…. Time
  Not so bad if constantly talking
  Makes bursting a pain, have to resend time each burst
  People like to burst, constant transmissions don't

## Slide 15: CDMA
Very large bandwidth
  So much it was initially thought to be a waste
Uses the large bandwidth really efficiently because…
  It's sharing it
One issue: near far issues
  Uplinks (reverse channel transmission) from MS that are far away
  Masked by near by MS
  Not so much an issue in reverse
  Solution: limit MS transmit power when nearby

## Slide 16: Two CDMA Styles
Frequency Hopping
  Not often used
  Requires very fast synthesizer
Direct Sequence
  Remain on a set frequency
  Leverage codes/dynamically assign them

## Slide 17: Spread Spectrum
CDMA suffers from near/far issue
Instead of blasting lots of data with super high power
  Use less power but more bandwidth
Digital signal s(t)
Code c(t)
Spreading signal m(t)
Spreading
Frequency
Power
Frequency
Power

## Slide 18: Frequency Hopping Spread Spectrum
Instead of spreading out over large bandwidth
  Splits over several channels
Hopping pattern
Spreading signal
Spreading
Transmitter
Frequency
Power
Digital signal s(t)
Despread
Receiver
Hopping pattern
Frequency
Power
Power
Digital signal
Frequency

## Slide 19: CDMA Example
Room with multiple people
Everyone understands English + 1 other language
Coordinator pairs up who can talk
So long as no pair is too loud…
  Everyone can talk at the same time
  Only the pairs can understand each other
  Even though there’s other conversations

## Slide 20: Next Time
Keep going with other signals
OFDM
SDMA
Amplitude Modulation
Frequency Modulation
Quadrature Amplitude Modulation