## Slide 1: Multi-Division Cont

## Slide 2: Review
FDMA
TDMA
CDMA
TDD
FDD

## Slide 3: OFDM
Orthogonal Frequency Division Multiplexing
FDM -> Frequency division
  Therefore… we’re diving things up by frequency
Divide a large piece of bandwidth
  Transmit several smaller bands at once
  Requires guard time between transmissions

## Slide 4: OFDM Pros/Cons
Pros
  Very efficient use of spectrum
  Time sync isn’t as critical
Problems
  Doppler shift
  Frequency mismatches
  Power/useage inefficient

## Slide 5: Space Division Multiple Access
I’m pointing my signal at YOU
  And only you…
Basically, directional antennas on BS and MS
  Can reuse channels
  No interference
  High quality signal
Problems
  Tech is fairly new
  How many antennas can you hang from a tower?

## Slide 6
MS1
MS2
MS3
BS
Beam 1
Beam 2
Beam 3

## Slide 7: Big Advantages of each:
FDMA
  Really easy
TDMA
  Flexible growth
CDMA
  Nearly unlimited growth?
SDMA
  Infinite capacity, pair with CDMA for extra goodness

## Slide 8: Problems
FDMA
  Wastes spectrum, guard bands, no changing frequencies
TDMA
  Needs guard space + time sync issues
CDMA
  Requires signal processing + power levels
OFDM
  Can be a power hog, can’t go fast
SDMA
  Mobile clients are tough to handle

## Slide 9: Where do we use them?
FDMA
  Radio & TV
TDMA
  Mostly GSM
CDMA
  2.5 and 3G Communications
OFDM
  The 4G’s
SDMA
  Satellites

## Slide 10: Amplitude Modulation
Ironic reality
  Very first technology used to transmit voice wirelessly
  We still use it today
This tells us how new this wireless tech really is!
Terms
  Amplitude
    Maximum extent of vibration or oscillation

## Slide 11: AM Signals
AM is a carrier wave that never changes
  It’s continuous, although unexciting
  We get the sound by modulating the carrier
  Modulate it with our “data”
Problem this leaves…
  Electromagnetic radiation exists all around us
  The purpose of AM’s carrier is to blend in with the natural environment
  Any receiver will also pickup this background noise
    And AMPLIFY it

## Slide 12: Frequency Modulation
Instead of compressing wave’s power, change how often we see the wave
  Aka, change the frequency
Huge signal-to-noise ration (SNR) bonus
  Less environmental factors to influence

## Slide 13: Crystal Radio
AM Radio receiver powered by AM radio waves
  No plugging in, no batteries, etc
Passive receiver
  Produce fairly weak sound
Active receivers
  Use power to amplify signal or audio through speakers

## Slide 14: Mobile Roaming

## Slide 15: What we’ve covered
What the spectrum is
How spectrum is divided/shared
Protocols used to actually make the sharing work
Basic communication methods of mobile devices
Problems that can exist with wireless communication

## Slide 16: Where we’re going next
Cellular specific stuff
  How the phone infrastructure works
  Devices roaming on wireless networks
  Handling massive data duplication to several devices
Femtocells/microcells
Network protocols used for communication
Infrastructure needed for cellular networks
802.11
Other wireless tech

## Slide 17: MS Mobility
Ideally… a MS can communicate with the world
  From anywhere in the world
  While moving someplace else in the world
Factors that impact this:
  Coverage of cellular networks
  Algorithms for negotiating handoffs
    What protocol do you connect with?
  Routing traffic over wired backbone

## Slide 18: Review
Pieces of cellphone networks
  BS/MS
  Base Station Transciever System (BTS)
  Authentication Center (AUC)
    Auths people
  Equipment Identity Register (EIR)
    Can be combined with AUC
    Tracks devices
  Base Satiation Controller (BSC)
    Uplink of BTS
  Home Location Register (HLR)
    Where are you from?
  Visitor Location Register (VLR)
    Where are you currently?
  Mobile Switching Center (MSC)
    Controller of multiple BSC
  The gateway
    Link out to the world
      Typically: PSTN or ISDN

## Slide 19
MSC
…
HLR
VLR
EIR
AUC
Gateway MSC
MSC
…
PSTN/ISDN
BSC
BTS
BTS
BTS
MS
Base Station System
BSC
BTS
BTS
BTS
…
MS
Base Station System
…

## Slide 20: Outbound Connections
PTSN
  Public Switched Telephone Network
  Basically: all the telephone circuits in a network
  Analog
  Back from the golden days
  Depreciating
ISDN
  Integrated Services Digital Network
  Digital phone services
  Faster services
  Can operate over IP
  Integrates voice + data
  Many types of ISDN
    US mostly uses PRI (T1, T2, etc)